## Slide 1: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg

## Slide 2: What is the confusion regarding dB, dBm?
What does unit dB mean? A unit of measurement that expresses ratio of one quantity to another. Commonly used for measuring sound waves, wireless signals, communication systems and electrical signals.
How do you calculate? When the quantity is mentioned in power
  dB=10×log10​(P2 / ​P1​​)
    P2 is being measured against P1

## Slide 3: What is the confusion regarding dB, dBm?
What does unit dB mean? A unit of measurement that expresses ratio of one quantity to another. Commonly used for measuring sound waves, wireless signals, communication systems and electrical signals.
How do you calculate? When the quantity is mentioned in amplitude
  Factor 20 accounts for power being expressed as a square of amplitude
  dB=20×log10​(A2/ ​A​1)
    A2 is being measured against A1

## Slide 4: What is the confusion regarding dB, dBm?
dBm: The power of a signal in decibel relative to one milliwatt
  What is 0 dBm? It is exactly one milliwatt
How do you calculate?
  dBm=10×log10​(P/ 1mW​)
  Measuring quantity P (expressed in milliwatts also)
Commonly used in communication and embedded systems

## Slide 5: Examples
Question: A wireless communication system involves increasing the transmit power from 1 Watts to 10 Watts. Can you estimate what is the increase in power when expressed in dB?
Answer: P1 = 1 Watt; P2 = 10 Watt
Increase in transmit power for communication system
= 10 X log10​(10/1) = 10 dB

## Slide 6: Examples
Question: A transmitter is radiating signal of strength of power output of 50 milliwatts. Can you estimate the strength in dBm?
Answer: dBm=. 10×log10​(P/1 mW), P = 50 milliwatt
= 10×log10​(50 mW/1 mW)
= 10×log10​(50)
= 10 X 1.698
= 16.98 dBm

## Slide 7: What kind of operations can you perform?
Can you add two terms together?
  dB and another dB term
  Sure! No Issues
Question: A wireless communication system involves increasing the transmit power from 1 Watts to 10 Watts, and then increasing from 10 Watts to 100 Watts. Can you estimate change in dB?
Answer: P1 = 1 Watt; P2 = 10 Watt, P3 = 100 Watt
dB1 = 10 X log10​(10/1) = 10 dB, dB2 = 10 X log10​(100/10) = 10 dB
Resulting gain in dB = dB1 + dB2 = 20 dB
dB3 = 10 X log10​(P2/P1) = 10 X log10​(100/1) = 20 dB

## Slide 8: What kind of operations can you perform?
Can you add two terms together?
  dB and another dB term, or dBm and another dBm term
  Sure! No Issues
Question: A wireless communication system involves increasing the transmit power from 50 milliwatts by another 50 milliwatts, what is resulting increase in dB and final strength in dBm?
Answer: P1 = 50 mW, Increase = 50 mW, P2 = 100 mW
P1 = 50 mW, 16.98 dBm, Increase of 50 milliwatt, We just cannot add P1 (dBm)+P1 (dBm)+ to get resulting signal strength. Poutput != 34 dBm
dBm (Final)= 10×log10​(P2/1 mW)
= 10Xlog10​(100 mW/1 mW) = 20 dBm

## Slide 9: What kind of operations can you perform?
Can you add/substract two terms together?
  dBm and another dBm term
  NO! Values are logarithmic representations of power. When you want to combine power, levels expressed in dBm, you first need to convert them back to linear scale (milliwatts), add them, and then convert the sum back to dBm.
Question: A wireless communication system involves increasing the transmit power from 50 milliwatts by another 50 milliwatts, what is resulting increase in dB and final strength in dBm?
Answer: P1 = 50 mW, Increase = 50 mW, P2 = 100 mW
P1 = 50 mW, 16.98 dBm, Increase = 10 log10​(100/50) = 10 X 0.301 = 3.01 dB
dBm (Final)= 10×log10​(P2/1 mW)
= 10Xlog10​(100 mW/1 mW) = 20 dBm

## Slide 10: What kind of operations can you perform?
Can you add/substract two terms together?
  dBm and another dBm term
  NO! Values are logarithmic representations of power. When you want to combine power, levels expressed in dBm, you first need to convert them back to linear scale (milliwatts), add them, and then convert the sum back to dBm.
Question: A wireless communication system involves increasing the transmit power from 50 milliwatts by another 50 milliwatts, what is resulting increase in dB and final strength in dBm?
Answer: P1 = 50 mW, Increase = 50 mW, P2 = 100 mW
P1 = 50 mW, 16.98 dBm, Increase = 10 log10​(100/50) = 10 X 0.301 = 3.01 dB
dBm (Final)= 10×log10​(P2/1 mW)
= 10Xlog10​(100 mW/1 mW) = 20 dBm

## Slide 11: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.