## Slide 1: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.

## Slide 2
Backscatter Like Transmission Mechanisms
Notes: ++ Over the past few years, I have designed several backscatter and beyond backscatter systems that precisely overcome these critical challenges that have limited the widespread deployment of backscatter on IoT devices.
++ The research vision that I have pursued and would like to pursue as a faculty member is to enable a massive deployment of IoT devices by bridging the energy asymmetry between sensing, computation and communication blocks by designing novel platforms and communication mechanisms. I am going to describe some of my research contributions next.

## Slide 3: What communication modality do these use?

## Slide 4: Communication using inductive coupling
A shared magnetic field is created between the two devices
  Change in current through one device induces current change through the other
  Device can vary load to transmit data
Very low frequency bands (135 KHz, 13.56 MHz)
  Transmit through materials including skin
  Sensitive to metal

## Slide 5: Near Field Communication (NFC)
Inductive Coupling concept (13.56 MHz)
  But attached to a powered and capable device (smartphone)
  10-20 cm range max (usually <10)
Can act as a tag or as a reader
  Allows smartphone to power a tag if needed
  Alternatively, smartphone could act like a card and respond to a reader
  Two smartphones can communicate without power transfer
Data rate 100-400 kbps!
  nRF52840 capable of 100 kbps communication with attached antenna

## Slide 6
Wireless communication using Light?
Notes: ++ Over the past few years, I have designed several backscatter and beyond backscatter systems that precisely overcome these critical challenges that have limited the widespread deployment of backscatter on IoT devices.
++ The research vision that I have pursued and would like to pursue as a faculty member is to enable a massive deployment of IoT devices by bridging the energy asymmetry between sensing, computation and communication blocks by designing novel platforms and communication mechanisms. I am going to describe some of my research contributions next.

## Slide 7: Light Fidelity (LiFi) for Internet of Things
Illumination
Energy
Communication
00100111
0
1
0
0
0
1
1
1
Advantages:
Light-fidelity
Notes: Let’s start the background story from LiFi
Light fidelity is a wireless technology that uses visible light for data transmission. The information is modulated on the light signal according to the baseband signal.
LiFi offers advantages, such as using a different part of the specturm other than crowded RF electromagnetic signal
In addtion, it simultaneously provide, illumination, energy and communication
Which makes it a good candidate for IoT connectivity.

## Slide 8: LiFi communication suffers from coverage challenges
Light cannot propagate through walls or other such physical boundaries
  Great from privacy perspective, but limits deployable location of IoT devices
Many IoT devices are located in places with very poor light propagation
  IoT devices that are located in the air vents
  Inside the wall, floor and other surfaces
  IoT devices that are embedded inside the human body
Notes: Light signal can not propagate through physical spaces. Things like walls, floors, metals block light signal.
When considering privacy, this is an advantage. However for IoT applications, it limits the scenarios where sensors located in places with poor light propagation.

## Slide 9: Question
A wireless IoT network uses a TDMA-based medium access protocol. The network has the following configuration:
  6 sensor nodes
  Each node periodically transmits a packet lasting exactly 5 ms
  Each node transmit every 100 ms (i.e., one packet per node every 100 ms).
Synchronization requires adding a guard interval of 1 ms between adjacent time slots to prevent collisions due to timing inaccuracies.

## Slide 10: Question
Consider a battery-powered IoT sensor node that periodically transmits environmental data to a gateway. Its radio operates in four different states with distinct current consumptions:
  Transmit (Tx) 25 mA
  Receive (Rx) 20 mA
  Idle Listening 2 mA
  Sleep 0.01 mA (10 µA)

## Slide 11: Question
Transmission cycle (occurs every 60 seconds):
Transmit data packet: 100 ms
Immediately after transmission, wait in Receive state for ACK: 50 ms
The node periodically checks the channel (Idle Listening) every 5 seconds for a duration of 20 ms.
For the rest of the cycle time, the node remains in Sleep mode.
Battery:
• Capacity clearly stated as 600 mAh (typical CR2450 coin cell).

## Slide 12: Question
1. Calculate average current of the node over one full 60-second cycle
2. Estimate battery life in days, given the average current you calculate
3. Clearly evaluate how reducing the Idle Listening interval frequency (e.g., sampling every 10 s instead of every 5 s) affects battery life

## Slide 13
Communication Layers
Notes: ++ Over the past few years, I have designed several backscatter and beyond backscatter systems that precisely overcome these critical challenges that have limited the widespread deployment of backscatter on IoT devices.
++ The research vision that I have pursued and would like to pursue as a faculty member is to enable a massive deployment of IoT devices by bridging the energy asymmetry between sensing, computation and communication blocks by designing novel platforms and communication mechanisms. I am going to describe some of my research contributions next.

## Slide 14: Introduction to communication layers
Communication between computing devices involves a structured set of procedures known as communication layers. These layers define how data travels from one system to another across networks. A standardized approach to networking ensures interoperability, efficiency, and reliability
A commonly used model is OSI or Open System Interconnection which divides the communication procedures into various different layers

## Slide 15: Why have a layered approach to communication?
• Simplifies complexity: Each layer focuses on specific functions
• Facilitates interoperability: Layers are standardized and interoperable between different systems
• Allows easier troubleshooting: Issues are isolated within a specific layer
• Promotes modularity: Layers can evolve independently without impacting the entire system

## Slide 16: Open System Interconnection Model
OSI model divides communication tasks into seven different layers

## Slide 17: Open System Interconnection Model
1. Application Layer: Interacts with user applications (e.g., HTTP, FTP, email protocols)
2. Presentation Layer: Formats or translates data into an appropriate form (e.g., encryption/decryption, data compression)
3. Session Layer: Manages communication sessions between applications (establishes, maintains, and terminates sessions)

## Slide 18: Open System Interconnection Model
The Transport Layer ensures efficient communication between endpoints:

## Slide 19: Open System Interconnection Model
The Transport Layer ensures efficient communication between endpoints:
TCP (Transmission Control Protocol):
• Connection-oriented
• Guarantees data integrity through acknowledgments and retransmission
• Ideal for email, file transfers, web browsing
UDP (User Datagram Protocol):
• Connectionless, fast delivery without guaranteed delivery or order
• Ideal for streaming media or gaming applications

## Slide 20: Open System Interconnection Model
The Transport Layer ensures efficient communication between endpoints:
TCP (Transmission Control Protocol):
• Connection-oriented
• Guarantees data integrity through acknowledgments and retransmission
• Ideal for email, file transfers, web browsing
UDP (User Datagram Protocol):
• Connectionless, fast delivery without guaranteed delivery or order
• Ideal for streaming media or gaming applications

## Slide 21: Open System Interconnection Model
Network Layer determines how data moves through interconnected networks:

## Slide 22: Open System Interconnection Model
Network Layer determines how data moves through interconnected networks:
IP (Internet Protocol):
• Assigns unique addresses (IP addresses) to devices
• Routes packets efficiently from source to destination
• Supports both IPv4 (32-bit addresses) and IPv6 (128-bit addresses)

## Slide 23: Open System Interconnection Model
Data Link Layer is responsible for packaging data into frames, managing direct communication between adjacent network devices, handling error detection and correction, and coordinating access to shared media (e.g., Ethernet, WiFi)
Core functions of data link layer are as follows:
Framing:
• Groups bits into structured “frames”.
• Adds headers and trailers for addressing and error-checking
Logical Link Control (LLC):
• Manages communication flow between sender and receiver
• Handles error detection, correction, and acknowledgments
Media Access Control (MAC):
• Regulates device access to shared media (wired or wireless)
• Ensures orderly transmission of data

## Slide 24: Open System Interconnection Model
Data Link Layer is responsible for packaging data into frames, managing direct communication between adjacent network devices, handling error detection and correction, and coordinating access to shared media (e.g., Ethernet, WiFi)
What are some examples of Data-link protocols?

## Slide 25: Open System Interconnection Model
Data Link Layer is responsible for packaging data into frames, managing direct communication between adjacent network devices, handling error detection and correction, and coordinating access to shared media (e.g., Ethernet, WiFi)
What are some examples of Data-link protocols?
• Ethernet defines how devices format data into frames for wired local networks, managing frame structure, addressing, and media access (MAC).
• WiFi (IEEE 802.11) protocols similarly manage framing, addressing, error detection, and media access for wireless communication.

## Slide 26: Data Link Layer – Framing Data
Converts arbitrary streams of data bits into structured frames
• Frame includes headers with addressing, control, error-checking information
• Ensures data integrity through checksums (CRC - Cyclic Redundancy Check)
Typical Ethernet Frame Structure:
Preamble | Destination Address | Source Address | Type/Length | Data | CRC

## Slide 27: Data Link Layer - Wireless Considerations
Wireless communication introduces unique challenges:
• Robustness:
  • Frames require additional control data to handle physical layer variations (e.g., varying signal strength and interference)
  • Different modulation rates might be used for different packet segments (headers might be transmitted at lower rates to enhance reliability)
• Explicit Routing Information:
  • Supports multi-hop wireless networks (e.g., mesh networks)
  • Ensures packets follow a defined route for optimal reliability

## Slide 28: Data Link Layer - Error Detection and Recovery
Effective communication requires identifying, managing transmission errors:
Error Detection:
  • Techniques such as CRC and checksums
  • Quickly identifies corrupted data for retransmission
• Error Recovery:
  • Automatic Repeat Request (ARQ) mechanisms
  • Retransmits corrupted data or missing packets
• Significance for Wireless:
  • Wireless communication experiences higher error rates due to environmental factors
  • Efficient recovery strategies are essential to reduce costly retransmissions

## Slide 29: Data Link Layer – Medium Access Control
MAC protocols handle device access to shared communication channels to prevent collisions and ensure efficient utilization:
Why MAC is essential:
  • In wired Ethernet, MAC ensures orderly data transmission on a shared cable
  • In wireless, MAC protocols coordinate transmissions to avoid interference and collisions

## Slide 30
Need for Medium Access Control
Notes: ++ Over the past few years, I have designed several backscatter and beyond backscatter systems that precisely overcome these critical challenges that have limited the widespread deployment of backscatter on IoT devices.
++ The research vision that I have pursued and would like to pursue as a faculty member is to enable a massive deployment of IoT devices by bridging the energy asymmetry between sensing, computation and communication blocks by designing novel platforms and communication mechanisms. I am going to describe some of my research contributions next.

## Slide 31: Medium access control for wireless is hard
Wired networks are constant, reliable, and physically isolated
  Ethernet has the same throughput minute-to-minute
  Bits sent through Ethernet or USB are (usually) received
Lack of wires introduces variability, unreliability, and vulnerability to interference compared to wired communication
Wireless networks are variable, error-prone, and shared
  WiFi throughput changes based on location and walls
  Signals from nearby devices interfere with your signals
  Individual bits might flip or never be heard at all
  Wireless signals degrade with distance, obstacles, and interferences

## Slide 32: Wireless is a shared medium
Wired communication has signals confined to a conductor
  Copper or fiber
  Guides energy to destination
  Protects signal from interference
Wireless communication is inherently broadcast in nature
  Energy is distributed in space
  Because signals are broadcast, interference and collisions are significant issues
  Signals also must compete with other signals in same frequency band
  Broadcast nature also raises privacy and security considerations

## Slide 33: Increasing network capacity is challenging
Wired networks just add more wires
  Buses are many signals in parallel to send more data
Wireless networks are harder
  Adding more links increases interference
  Need to expand to different frequencies

## Slide 34: Analogy: wireless medium as acoustic
How do we determine who gets to speak?
  If two or more devices transmit simultaneously, their signals overlap, and the communication fails
Eye contact (or raise hand) -> out-of-band communication
Waiting for silence before speaking -> carrier sense multiple access
Having pre-scheduled speaker turns -> time division multiple access
Just speak and hope it works -> ALOHA
Everybody sing at different tones -> frequency division multiple access (stretching the metaphor)

## Slide 35: Wireless: Medium and multiple access challenge
Problem: Multiple radio transmitters want to access a common channel
  How to coordinate access for these radio transmitters ?
  MAC protocols ensure orderly, efficient sharing of limited wireless bandwidth

## Slide 36
Channelization Protocols

## Slide 37: FDMA – Frequency Division Multiple Access
Separate transmissions by placing them at different frequencies
Channel:
Technically, each device can use a separate, fixed frequency
  One example can be walkie-talkies
  What are disadvantages of giving every device own frequency?
Conceptually, how RF channels work
  WiFi networks pick different bands
  802.15.4 picks a channel to communicate on

## Slide 38: FDMA – Frequency Division Multiple Access
Separate wireless transmissions by placing them at different frequencies
Channel:
Technically, each device can use a separate, fixed frequency
  One example can be walkie-talkies (mostly separate)
  What are disadvantages of giving every device own frequency?

## Slide 39: Wireless communication over multiple channels
Why do we need multiple channel for wireless communication?
  Increase throughput
  spatial diversity
  Increase reliability

## Slide 40: Multi Channel MAC Protocols
Use a control channel:
  Use of a default channel and time synchronization for control message exchange
  Nodes switch to a different channel for data communication
All channels are used for data communication:
  Nodes switches to another channel when link quality is bad
  How do we find a “good” channel to switch to?

## Slide 41: Wifi Channels
14 channels designated in the 2.4 GHz range spaced 5 MHz apart (with the exception of a 12 MHz spacing before channel 14)
https://en.wikipedia.org/wiki/List_of_WLAN_channels

## Slide 42: ZigBee Channels

## Slide 43: TDMA – Time Division Multiple Access
Split transmissions in time
  Devices share the same channel
Splits time into fixed-length windows
  Each device is assigned one or more windows
  Can build a priority system here with uneven split among devices
Requires synchronization between devices
  Often devices must listen periodically to resynchronize
  Less efficient use of slots reduce synchronization
    Large guard windows. E.g. 1.5 second slot for a 1 second transmission

## Slide 44: TDMA: Time Division Multiple Access‏
Consider a 1Mbps channel (1,000,000bits/sec)
Divide channel into 1000 (equal) times slots
Each slot is 1ms, and can transmit 1,000 bits
Assign slots to 50 users
  Each user transmits every 50 slots/ms and transmit 20 times/slots per second
  On average, each user can transmit 20kbps
Buffering is needed on both sender and receiver to match the differences in data rates
  sender-side: 20kbps -> 1 Mbps
  Receiver-side: 1Mbps -> 20kbps
Notes: 44
44

## Slide 45: TDMA vs. FDMA
Time
Frequency
In practical systems, TDMA is often combined with FDMA
Frequency
Time
FDMA
Time
Frequency
TDMA
Notes: 45
45

## Slide 46: Orthogonal Frequency Division Multiplexing :OFDM
In FDM, the entire frequency spectrum is dedicated to carry data from a single source
  Example: transmit at 40Mbps over a 20 MHz spectrum
In OFDM, data is divided into many (slower) bit streams and multiple subcarriers (each with smaller spectrum) is used
  Example: divide data source into 40 sources, each 1Mbps

## Slide 47: WiFi Channel Usage

## Slide 48: Cross Channel Interference (CTI)
A. Hithnawi, et.al.,TIIM: Technology-Independent Interference Mitigation for Low-power Wireless Networks, IPSN 2015

## Slide 49: Frequency and Time leads to Spread Spectrum (SS)
Spread-spectrum techniques are methods by which a signal is deliberately spread in the frequency domain, resulting in a signal with a wider bandwidth
Such techniques can be used to establish secure communications, increase resistance to natural interference, jamming and to prevent detection
Concept has been alluded to in 1900s, and applied in some form during WWII
Resistant to narrowband interference
Signals are difficult to interpret – appears as if increase in background noise
Can share frequency band with others with minimal interference

## Slide 50: Spread spectrum: Frequency Hopping (FH)
FHSS increase resistance to a) natural interference b) jamming c) detection

## Slide 51: Spread spectrum: Frequency Hopping (FH)
A protocol that we use everyday uses Frequency hopping spread spectrum technique?

## Slide 52: Spread spectrum: Frequency Hopping (FH)
A protocol that we use everyday uses Frequency hopping spread spectrum technique?
Bluetooth hops between 79 different 1 MHz channels in the band.

## Slide 53: Spectral efficiency
Spectral efficiency (in bits/s/Hz) determines how efficiently devices utilize allocated bandwidth, depending on the modulation scheme
Different modulation schemes provide different spectral efficiency:
  Simple modulation (e.g., FSK) ≈ 1 bit/s/Hz.
  Advanced modulation (e.g., QPSK, QAM) higher bits/s/Hz (2–8 bps/Hz).

## Slide 54: Question
Total available bandwidth: 500 kHz
4 IoT nodes:
  • Node A and B each need 50 kbps
  • Node C needs 100 kbps
  • Node D needs 200 kbps
The chosen modulation scheme supports a maximum spectral efficiency of 1 bit/s/Hz (for simplicity), meaning each 1 Hz of bandwidth can carry 1 bit per second.

## Slide 55: Question
Calculate how much frequency bandwidth each node must be allocated based on the given spectral efficiency (1 bps/Hz)
Verify if the allocated bandwidth fits within available 500 kHz channel
If an additional node (Node E) joins later and requires 200 kbps, clearly evaluate if it’s feasible to accommodate this node

## Slide 56: Question
A wireless IoT network uses a TDMA-based medium access protocol. The network has the following configuration:
  6 sensor nodes
  Each node periodically transmits a packet lasting exactly 5 ms
  Each node transmit every 100 ms (i.e., one packet per node every 100 ms).
Synchronization requires adding a guard interval of 1 ms between adjacent time slots to prevent collisions due to timing inaccuracies.

## Slide 57: Question
1. Calculate the total TDMA frame duration clearly, including guard intervals.
2. Clearly evaluate channel utilization efficiency (actual data transmission time vs. total frame time, including guard intervals).
3. Determine clearly the worst-case latency a node experiences from packet generation to successful transmission.
4. Suppose the synchronization overhead (guard interval) can be reduced from 1 ms to 0.2 ms by using a more accurate synchronization mechanism:
  • Clearly recalculate channel utilization and latency.
  • Clearly discuss the trade-offs involved (complexity, cost, energy).

## Slide 58
Random Access Protocols

## Slide 59: Why Do We Need Random Access Protocols (RAP)?
• Networks are increasingly wireless and dynamic:
  • Rapid proliferation of mobile devices, sensors, and IoT nodes
  • Devices join or leave networks unpredictably; traffic patterns not always regular/ predictable
• Fixed scheduling is challenging or impractical:
  • Pre-allocating transmission slots becomes inefficient when traffic is bursty/unpredictable
  • Scheduled transmissions waste resources if nothing to send during allocated slots
• RAPs provide an efficient, lightweight solution for managing sporadic, unscheduled, low-rate data transmissions
• Examples of scenarios benefiting from Random Access:
  • Smart-home IoT sensors sending occasional status updates
  • Low-power wide-area networks (LPWANs) in environmental monitoring (e.g., LoRaWAN)

## Slide 60: Analogy to understand Random Access Protocols
Imagine a conversation in a crowded room:
Scenario: Several people want to speak occasionally, but unpredictably
• Scheduled speaking (like TDMA): Each person has a fixed speaking slot
Issue: Wastes time if some people have nothing to say
• Random speaking (like ALOHA): Speak when needed, and if there’s a collision,
pause and retry after a random interval
Benefit: Low overhead, simple, easy to manage with minimal coordination

## Slide 61: Random access protocol: Aloha
• Origin & Historical Context:
  • Developed in 1971 at the University of Hawaii by Norman Abramson
  • Designed originally to connect computers across islands using radio links (ALOHAnet)
• Core Idea (simplicity first):
  • Devices transmit whenever data is available, without explicit coordination
  • No prior scheduling or channel sensing; purely random transmissions
• Why ALOHA matters historically:
  • First practical implementation of random access wireless networking
  • Inspired modern random-access protocols, foundational for today’s wireless systems (BLE, LoRaWAN, satellite networks)

## Slide 62: Random access protocol: Aloha
Protocol Rules:
1. If you have data, transmit immediately
2. After transmission, wait a certain time to receive acknowledgment (ACK)
3. If ACK is received, transmission successful; if no ACK, wait a random time interval and retransmit (exponential backoff recommended)
• Collision Problem:
  • If two or more nodes transmit simultaneously, collision occurs, resulting in lost data
  • Nodes do not listen before transmitting (no channel sensing)

## Slide 63: Packet collisions are bad, we need to avoid them
Each packet transmission has a window of vulnerability
  If two nodes transmit within one packet-duration interval, collision occurs
  The time duration is the the on-air duration of a packet
  Competing transmissions during the packet are bad
  Competing transmissions before packet can also be bad

## Slide 64: Solution to this problem? Dividing time in slots
Slotted ALOHA reduces collision windows by aligning transmissions to predefined slots
Requires synchronization: Every device must know slot boundaries, adding complexity to the implementation and device
Real world Analogy: Speaking during predefined time slots in a conference
time

## Slide 65: ALOHA throughput
It can be shown that traffic maxes out at
  ALOHA: 18.4%
  Slotted ALOHA: 36.8%
Assuming Poisson distribution of transmission attempts
Slotted throughput is double because the “before” collisions can no longer occur

## Slide 66: Why Use Random Access if Efficiency is Limited?
Simplicity and low overhead:
  • RAPs do not need complex synchronization or scheduling mechanisms
  • Suitable for resource-constrained IoT or sensor networks
• Efficiency in low-load scenarios:
  • Collisions are rare when network load is low
  • Random access can achieve low latency for intermittent or bursty transmissions
• Real-world usage examples:
  • BLE beaconing: Short, random broadcasts to discover devices
  • LoRaWAN: Simplicity and battery efficiency preferred over maximizing throughput
  • Satellite and RFID networks: Sporadic data transmission scenarios

## Slide 67: Why Use Random Access if Efficiency is Limited?
Simplicity and low overhead:
  • RAPs do not need complex synchronization or scheduling mechanisms
  • Suitable for resource-constrained IoT or sensor networks
• Efficiency in low-load scenarios:
  • Collisions are rare when network load is low
  • Random access can achieve low latency for intermittent or bursty transmissions
• Real-world usage examples:
  • BLE beaconing: Short, random broadcasts to discover devices
  • LoRaWAN: Simplicity and battery efficiency preferred over maximizing throughput
  • Satellite and RFID networks: Sporadic data transmission scenarios

## Slide 68: CSMA/CA: Introduction and Motivation
What is CSMA/CA?
  • Carrier Sense Multiple Access with Collision Avoidance is a medium access control protocol widely used in wireless networks (especially WiFi)
  • Nodes sense the medium to check if it’s busy before attempting transmission, but collisions are actively avoided rather than detected after occurrence
Why is Collision Avoidance Necessary?
  • Wireless networks have difficulty reliably detecting collisions directly due to signal fading, interference, and hidden nodes.
  • Collision Avoidance proactively reduces the probability of collisions occurring

## Slide 69: How CSMA/CA Works (Step-by-Step)
1. Listen first (Carrier Sensing):
  Nodes listen (sense) the channel before transmission. If the channel is busy, the node waits.
2. Random Backoff (Collision Avoidance):
  Once the channel becomes idle, nodes don’t transmit immediately. Instead, they wait for a random time interval (random backoff period) before transmitting
3. Transmit Data:
  After the random wait, if the medium remains idle, the node transmits its data
4. Acknowledgment (ACK):
  Successful reception is confirmed through an ACK from the receiving node. Lack of ACK implies potential collision or error, triggering retransmission

## Slide 70: CSMA/CA: Choosing Wmax
Should Wmax be constant?
Intuitively, Wmax should be small when there is lower chance of collision and vice versa
Wmax varies according to the Binary Exponential Backoff (BEB) algorithm.
Set “slot time” to 2 times the max. propagation delay on the channel
    If this is the first transmission, sends immediately
    If there is a collision, after i-th collision, pick Wmax randomly between 0 and 2i-1 time slots.

## Slide 71: Binary Exponential Backoff (BEB) in CSMA/CA
Why Exponential Backoff?
  • If collisions occur, waiting intervals adaptively increase to further reduce future collision probability
  • Each successive collision indicates higher channel contention
BEB Mechanism clearly explained:
1. Initial attempt: Small waiting period (randomized within a small range).
2. After each collision:
  The range (window size) for the random backoff doubles (exponential increase), reducing collisions progressively:
  • 1st collision: Wait between 0 - (2^1-1) slots
  • 2nd collision: Wait between 0 - (2^2-1) slots
  • After i-th collision: Wait between 0 - (2^i-1) slots.

## Slide 72: CSMA/CA: Trade-off
What are the Trade-off:
  More aggressive (smaller Wmax) – more likely to achieve higher channel utilization, but also more likely to collide
  Less aggressive – lower channel utilization, less likely to collide
Utilization vs. delay
  Overly aggressive or conservative can increase delay
Optimal point depends on
    Number of stations/nodes contenting
    Traffic load

## Slide 73: Hidden terminal problem
Device A
Device B
Device C

## Slide 74: CSMA with RTS/CTS
Occurs when two transmitters cannot sense each other’s transmissions but interfere at a common receiver
RTS/CTS Mechanism:
  • Request to Send (RTS): Short control frame sent by transmitter requesting access
  • Clear to Send (CTS): Receiver replies if it’s ready, informing nearby nodes to remain silent temporarily
A partial solution
  When channel is idle, transmitter sends a short Request To Send (RTS)
  Receiver will send a Clear To Send (CTS) to only one node at a time
  RTS collisions are faster and less wasteful than hidden terminal collisions
  Downside: overhead is high for waiting for CTS when contention is low

## Slide 75: Solving Hidden Terminal Problem
A
B
C
RTS
CTS
CTS
OK, I’ll wait …

## Slide 76: Real-world protocol access control
ALOHA
  BLE advertisements
  Unlicensed LPWANs: Sigfox, LoRaWAN
CSMA
  WiFi (slotted, CSMA/CA)
TDMA
  BLE connections
  Cellular LPWANs: LTE-M and NB-IoT

## Slide 77
Medium Access Control for Internet of Things

## Slide 78: Medium access control for Internet of Things
• General wireless MAC protocols typically optimize for:
  Low Latency
  High Channel Utilization
  Fairness (all nodes have equal chance to communicate)
However, IoT has unique requirements:
  Extremely low power consumption
  Typically, low and intermittent channel utilization
Priority shift for IoT MAC protocols:
  Energy conservation becomes the primary design goal
  MAC protocols must minimize power usage to prolong battery life

## Slide 79: Energy consumption of medium access control
Sources of energy consumption in contention-based protocols:
  1. Overhearing (receiving unintended transmissions)
  2. Control packet overhead (RTS, CTS, ACK, etc.)
  3. Data transmission/reception
  4. Idle listening (listening to channel when nothing is being transmitted)
(1) – (3) occurs only when there is an active transmission
(4) (Idle listening) happens even without any transmissions and can dominate energy use

## Slide 80: “Life Cycle” of MAC Protocols
(4)
(1) – (3)
(4)
(1) – (3)
(4)
(1) – (3)
Less Traffic
(4)
(1 – (3)
(4)
(1) – (3)
Less Traffic
(4)
(4)
As traffic load decreases, the proportion of energy consumed by idle listening increases significantly. This makes idle listening the dominant source of wasted energy in low-load IoT networks.

## Slide 81: Idle listening is energy expensive
Idle listening consumes significant energy, especially at low load:
  • Measurements show idle listening can consume between 50% to 100% of the energy needed for actual receiving
• Dilemma clearly presented:
  • If nodes turn off their radios to save power, how will they detect incoming transmissions?
Solution Needed:
  Duty cycling—periodically waking up briefly to sense transmissions, then returning to sleep mode

## Slide 82: Duty cycled medium access control protocols
Core Concept:
  Nodes sleep when inactive, drastically reducing idle listening time
  Periodically “wake up” to sense channel activity
Main advantage:
  Minimizes idle energy consumption
• Key challenge:
  Determining the optimal wake-up schedule is critical
  Coordination required to ensure nodes wake at the right time to detect transmissions

## Slide 83: ALOHA with Preamble Sampling
Vanilla Aloha: Works when a) There is no contention (usually true when utilization is low) b) Receiver is listening (may not be true duty cycling)
How to convert ALOHA to work with duty cycle?

## Slide 84: ALOHA with Preamble Sampling
Vanilla Aloha: Works when a) There is no contention (usually true when utilization is low) b) Receiver is listening (may not be true duty cycling)
How to convert ALOHA to work with duty cycle?
  Nodes periodically wake and sample the channel to check for activity
  Transmitters send an extended preamble (long duration) before data, ensuring receivers detect transmissions
• How it works step-by-step:
  • Sender transmits a long preamble to “wake up” receiver
  • Receiver periodically wakes briefly to sense for preambles
  • Once a preamble is detected, receiver stays awake, receives the actual data, and acknowledges

## Slide 85: Aloha with Preamble Sampling
Preamble
Data
Sender
Receiver
Sensing
Sensing
Sensing
Sensing
Receiver 1
Sensing
Sensing
ACK
Recv
Receiver 2
Sensing
Sensing
Sensing

## Slide 86: Aloha with Preamble Sampling
• Advantages:
  • Reduces idle listening significantly, saving power
  • Simple to implement, asynchronous, no synchronization required
• Limitations:
  • Preamble wastes energy at sender and slightly increases latency
Preamble
Data
Sender
Receiver 1
Sensing
Sensing
ACK
Recv
Sensing
Tp
Ts
TD

## Slide 87: B-MAC: Asynchronous Medium Access Control
Implements preamble sampling concept.
  Nodes independently choose wake-up intervals (asynchronous).
Operational Steps:
1. Sender transmits a long preamble
2. Receivers periodically sample the channel
3. If a preamble is detected, the receiver stays awake for data transmission
Key Parameters:
  Channel sampling interval: Determines energy usage
  Long preamble: Duration matches sampling interval to ensure detection
Pros and Cons:
  Pros: Energy-efficient, simple, asynchronous operation
  Cons: Long preamble introduces latency and unnecessary overhead

## Slide 88: Improving B-MAC with X-MAC
X-MAC improves over B-MAC
  Sender transmits many “probes” with gaps between probes. Each probe contains address of intended receiver
  Receiver checks address embedded in probe, sends acks if it is the destination during the gap period between probes
  Sender transmits DATA, receive replies with Ack to complete data transfer

## Slide 89: ContikiMAC
ContikiMAC is the MAC protocol implemented in Contiki OS

## Slide 90: Synchronous MAC
Nodes agree to wake up simultaneously at predetermined intervals
Each interval split into active (listen period) and inactive (sleep period)
Example Scenario (clearly illustrated):
10% duty cycle: 10% of the time nodes listen; 90% sleep.
For example: nodes listen for 100 ms, then sleep for 900 ms.
Advantages:
  Predictable and coordinated
  Easier to manage communication during listening periods
Disadvantages:
  Requires synchronization overhead.
  Less flexible compared to asynchronous schemes (X-MAC, B-MAC)

## Slide 91: Synchronous MAC (SMAC)
Example: 10% duty cycle
  Each node listens for 100ms and sleep for 0.9s
  Each node listens for 1s and sleeps for 9s

## Slide 92: Question
Consider a wireless sensor network with the following characteristics:
  • Nodes follow a synchronized S-MAC schedule with a 10% duty cycle.
  • Total frame duration (Listening + Sleeping) = 1 second (1000 ms).
  • Therefore, nodes stay awake 100 ms and sleep for 900 ms per cycle.
Assume:
  • Each node has a fixed battery (1000 mAh) with radio current consumption of:
  Active listening/transmission: 20 mA
  Sleep mode: 0.05 mA
When active, the network sends data packets of duration 10 ms each.

## Slide 93: Question
1. Energy Calculation: Compute the average current consumption per node over one complete cycle (active + sleep) using the given parameters.
2. Battery Life Estimation: Given a sensor powered by a battery rated at 1000 mAh, estimate the node’s lifetime under these conditions (ignore battery inefficiencies).
3. Latency Considerations: If a critical event occurs immediately after the active listening period, what’s the maximum latency until the event is detected and reported?
4. Trade-offs clearly discussed: If you increase the duty cycle from 10% to 20%, how does this change your energy consumption and latency?

## Slide 94
Collisions are always bad?

## Slide 95: Receiving transmissions with collisions
• Occurs when multiple nodes transmit simultaneously, yet the receiver successfully decodes the strongest signal
• In some scenarios, collisions do not always cause complete failures
Receiver receives the strongest signal, ignoring weaker interfering signals
Enhances performance in certain scenarios (dense IoT deployments)

## Slide 96: Receiving transmissions with collisions
R
T2
-83.02dB
T1
-84.09dB
100%
35%
T3
-80.93dB
15%
T4
-70.89dB
99%

## Slide 97
Flooding

## Slide 98: Flooding is a recreation of broadcasts
Goal: get information to all nodes
  This is the problem of “data dissemination”
Problem: difficult in Mesh topologies
  Packet loss, retransmission delays
Really, data dissemination is just to broadcast to all nodes
  But broadcast transmissions don’t reach far enough to cover entire mesh

## Slide 99: Synchronous transmissions
Multiple nodes transmit same packet at same time
R can receive packet with high probability if Δ is small
  May even improve probability of reception (more energy at receiver)
500 ns is 1/32 of a symbol for 802.15.4 (chip duration)

## Slide 100: Fast packet propagation in Glossy

## Slide 101: Fast packet propagation in Glossy

## Slide 102: Fast packet propagation in Glossy

## Slide 103: Fast packet propagation in Glossy

## Slide 104: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.