## Slide 1: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg

## Slide 2: Discussion regarding the project
Deadline: April 26th April
Submission after deadline: No Penalty (Last date: 30th April)
Two tasks needs to be performed. Builds on previous assignments
To be submitted: Report, source code, demonstration, readme file

## Slide 3: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Routing Basics
Flooding
Reactive and Proactive routing

## Slide 4: Overview of Global Positioning System
Satellites placed in Medium Earth Orbit (20,000 KM)
  Orbit earth twice per day
  Placed such that 4 are in view everywhere, always
  31 total in orbit as of November 2020
    Most recent launch November 5th 2020
Comparisons
  LEO 200-2000 km, ISS at 340 km
  GEO 35,000 km

## Slide 5: What do you mean by the term localization?
Localization systems determine the physical coordinates of an electronic device such as IoT nodes, drones, mobile phones or a subject
These physical coordinates of electronic devices are:
  Global - aligned with some externally meaningful systems like GPS
  Relative - some “rigid transformation” (rotation, reflection, translation) away from a global coordinate systems
Localization indoors: goal is positioning things within a building
  Where can I find X?
  X: where am I located?
  X and Y: are we near each other?

## Slide 6: GPS PHY
GPS frequency
  1.2 GHz and 1.5 GHz
  10-15 MHz bandwidth
BPSK modulation
Signal has to travel 20,000 km, but most of that is through space
  Tx power 25 Watts (44 dBm)
  Rx sensitivity -140 dBm to -160 dBm (50 bps data rate)
  ~200 dBm total link budget

## Slide 7: GPS transmissions
Each satellite sends a unique pseudo-random number sequence
  Sequence repeats in time (over minutes) and is well-known
  Position in signal is used to calculate time of flight

## Slide 8: Problem with RSSI-based distance – not accurate
Pathloss is NOT only due to distance
RSSI is way worse at this than you hope it would be
Citation: literally everyone has made this figure at some point

## Slide 9: Time of flight (also known as time of arrival, ToA)
Determine distance by knowing:
  Exact position of infrastructure
  Transmit time
  Receive time
  Signal velocity (i.e. speed of light)
Infrastructure transmits and device listens
  Can happen all the time, but devices only listen when they want a position
Requires time synchronization between infrastructure and device
  Synchronization must be good: 1 μs = 300 meters

## Slide 10: Time difference of arrival (TDoA)
Device transmits and infrastructure receives transmission
  Multiple infrastructure nodes receive at different times based on distance
Determine distance by knowing
  Exact position of infrastructure
  Time of arrival at two different locations
  Signal velocity (i.e. speed of light)
Doesn’t require synchronization with infrastructure!
  Still requires synchronization between infrastructure nodes
  Does require device to transmit loud enough for infrastructure to hear it…

## Slide 11: Time difference of arrival with different mediums
Exploit differences in speed, say RF and audio
Example: Cricket System [1]
  In addition to a radio, each node also has a speaker and microphone
How does Cricket works?
Transmitter sends a radio message, waits some time (optionally) t_delay, sends audio “chirp” sound
Listener hears the radio signal, record time t_radio
Listener hears the audio signal, record time t_sound
[1] http://cricket.csail.mit.edu/

## Slide 12
Time diff between signal arrival = d/SSound – d/SRadio + tdelay
Works well in LOS environment
  Cricket (uses ultra sound) can obtain close to cm accuracy
Requires additional hardware and works better with calibration
Time difference of arrival with different mediums

## Slide 13: Angle of arrival (AoA)
Trilateration doesn’t only require distances, angles work
Antenna arrays can be used to determine the angle of an incoming signal
  Allows the use of normal RF communication (WiFi or BLE)
BLE 5.1 includes AoA localization

## Slide 14: Fingerprinting overview
At setup time, for many locations throughout building
  Measure signal strength to Access Point
  Record measurement in a database with location
At run time, for the device that wants a location
  Measure signal strength to Access Point
  Look up measurement in database to get location

## Slide 15: How to discover nodes or devices nearby
Scenarios for local discovery
  You just enter a shopping mall. You would like to check if there is WiFi service. How does your mobile phone discover the presence of WiFi networks?
  Small devices with low power network interface (e.g. ZigBee) are deployed in the surrounding and carried by humans. How can these devices discover other devices in range (in an energy efficient way)?

## Slide 16: How to perform neighbor discovery?
Problem is “easy” to solve if there is no constraint and all nodes can be active all the time.
  Challenge is to design a protocol that is energy efficient.
Two broad methods for local neighbor discovery:
  Synchronous
  Asynchronous

## Slide 17: Synchronous neighbor discovery
All nodes are synchronized to the same clock/time.
Nodes wakeup periodically at same time to transmit/receive packets
Node A discovers node B when it hears a transmission from node B
Example:
  Time divided into slots of 100ms and there is a global starting reference time t0 sec
  With a 10% duty cycle, period is 1s,
    each node wakes up at t0 + k sec for 100ms, where k = 0,1,2,3,4….
  With a 1% duty cycle, period is 10s,
    each node wakes up every t0 + 10k sec for 100ms, where k = 0,1,2,3,4….

## Slide 18: Drawbacks to synchronous neighbor discovery?
Synchronization can be expensive and periodically re-synchronization will be needed to correct for clock drift over time
As all nodes wakeup at the same time to transmit/receive, collision may increase if too many node transmit simultaneously

## Slide 19: Asynchronous Protocols
Challenges:
  No time synchronization
  All nodes are resource constrained
Assumptions
  Divide into time slots (e.g. 100ms)
  Each device decides (randomly?) which time slots to wakeup to transmit/listen
How long will two such devices take to discover each other?

## Slide 20: Birthday Paradox
In a group of N people, what is the probability that there is at least one pair of people who have the same birthday? (assume 365 days in a year)
In general, Prob = 1 – P(none of the N people have the same birthday)
  N = 2, Prob = 1 – (364/365)
  N = 3, Prob = 1 – (364/365)(363/365)
  N = 4, Prob = 1 – ((364/365)(363/365)(362/365)
  N = n, Prob = 1 – 365!/(365n(365-n)!)
Example:
  N = 2, Prob = 0.0027
  N = 23, Prob = 0.5073
  N = 50, Prob = 0.9704

## Slide 21
“Birthday” Protocol
Easy to implement
Good average discovery latency but unbounded worst case

## Slide 22: DISCO - Asynchronous neighbor discovery algorithm
Scheduling radio wake times at multiples of prime numbers to ensure deterministic discovery
  Nodes can have different duty cycles
Version 0: A node i picks a prime number, say pi and wakes up pi timeslots, the duty cycle is (1/ pi). In the worst case, two nodes pi and pj will meet after (pi * pj) timeslots.
  Problem: what if both nodes pick the same prime number?
Version 1: A nodes i picks a prime number, say pi1 and pi2 (pi1 != pi2), wakes up every pi1 and pi2 timeslots. The duty cycle is (1/pi1 + 1/pi2)
  If both nodes pick the same pair of prime number:
    Duty cycle ~ (pi1 + pi2)/ pi1 pi2, Worst Case ~ pi1 pi2
Dutta, Prabal, and David Culler. "Practical asynchronous neighbor discovery and rendezvous for mobile sensing applications." Proceedings of the 6th ACM conference on Embedded network sensor systems. 2008.

## Slide 23: Example application: air quality monitoring
[1] Cheng et al. AirCloud: a cloud-based air-quality monitoring system for everyone. 2014. [2] Purple Air. 2019.
[1]
[2]
[2]

## Slide 24: We need another network option
Requirements:
Wide area of coverage
  Deploy fewer gateways
Low power
  So we can deploy on batteries
Doesn’t need high throughput
  Sensor data is relatively small

## Slide 25: Long-range,low-data needs are not easily met
Bluetooth
WiFi
3G
4G
BLE
Zigbee
Low-Power Wide-Area Networks
2G
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost

## Slide 26: Long-range, Low-power: design choices
How would you design PHY for long-range, low-power ?
  Modulation
    Unclear. Perhaps, not complicated or complex (simple devices)
  Tx Power
    High (much higher than 0 dBm)
  Carrier Frequency Band
    Low (something lower than 2.4 GHz, 915 MHz or lower?)
  Data Throughput
    Low (much lower than 1 Mbps)
  Channel Bandwidth
    Unclear. Likely smaller for lower frequency carrier.

## Slide 27: Design a low-power wide-area network
Any particular MAC choices for lower power?
  Diversity of devices in network
    High power gateway, low power devices in star topology
  Devices should be off whenever possible
    Listen-after send for downlink
  Remove requirements for synchronization
    No TDMA access control if it can be avoided
    Aloha, CSMA

## Slide 28: Long-range CSMA is problematic
Long-range makes everything more challenging
  Kilometers of range mean kilometers between devices
Detection of channel use is less reliable
  Active research in clear channel assessment for LPWANs
Hidden terminal problem has a wider range
  Might make RTS/CTS more important
Result: CSMA doesn’t dominate LPWANs like it does WLANs

## Slide 29: LPWANs overview (common qualities)
Unlicensed 915 MHz band (902-928 MHz)
Higher power transmissions: ~20 dBm (100 mW)
Low data rate 100 kbps or less
Range on the order of multiple kilometers
Simple Aloha access control

## Slide 30: LoRaWAN
Open communication standard built with proprietary LoRa PHY
Operates in the unlicensed band
Low data rate (1-20 kbps) and long range (~5 km)
Most popular LPWAN protocol
  Academic research and industry involvement

## Slide 31: LoRa employs a different modulation scheme
Chirp Spread Spectrum (CSS): Modulation technique where frequency is varied linearly from lowest to highest within a channel

## Slide 32: Spreading factor of CSS modulation
Spreading Factor is essentially the rate-of-change of frequency
  Slope of the line
  Lower values of spreading factor (steeper slope) are faster data rate
Important: different spreading factors are (mostly) orthogonal!
  Two can overlap in time, space, and channel without a collision

## Slide 33: LoRa data rates
Data Rate Index | Spreading Factor | Bit Rate
125 kHz Uplink Rates |  | 
0 | SF10, 125 kHz | 980 bps
1 | SF9, 125 kHz | 1760 bps
2 | SF8, 125 kHz | 3125 bps
3 | SF7, 125 kHz | 5470 bps
500 kHz Uplink Rates |  | 
4 | SF8, 500 kHz | 12500 bps
500 kHz Downlink Rates |  | 
8 | SF12, 500 kHz | 980 bps
9 | SF11, 500 kHz | 1760 bps
10 | SF10, 500 kHz | 3900 bps
11 | SF9, 500 kHz | 7000 bps
12 | SF8, 500 kHz | 12500 bps
13 | SF7, 500 kHz | 21900 bps
Data rate depend on channel in use, spreading factor
64-channel uplink
  1-5 kbps data rate

## Slide 34: LoRaWAN MAC
Uplink: Aloha - transmit whenever
  Randomly split across 64 uplink channels (reduced odds of collision)
  Devices a different spreading factors also do not collide
  Packets are very long though: up to 400 ms in duration
Downlink: listen-after-send (class A device)
  Two windows for RX on different channels

## Slide 35: LoRa link budget and transmission range
Typical TX power 20 dBm
  Up to 30 dBm for 64-channel hopping
  Up to 26 dBm for 8-channel hopping
Receive sensitivity -119 dBm/-146 dBm (highest SF)
  Compare to -100 dBm for 802.15.4 and -95 dBm for BLE
Resulting range is kilometers in urban environments

## Slide 36: LoRaWAN network providers
Network provides with a deployment of gateways
  The Things Network (predominantly in Europe)
  Helium
    Any can buy and install their own gateway, which serves everyone
    Microtransactions to pay for communication

## Slide 37: Sigfox
Very low-rate (600 bps), very long-range (10+ km) communication
Star-topology networks, with always-listening gateways
  Any number of low-power end devices
Uplink-focused communication
Applications: very low-rate metering

## Slide 38: Sigfox PHY
Unlicensed-band communication
  Europe 868 MHz. US 902-928 MHz (915 MHz band)
Ultra-narrowband 600 Hz (100 Hz Europe) channel bandwidth
  Detection only needs to occur at very specific frequency
  Helps improve signal-to-noise ratio

## Slide 39: Sigfox unbalanced uplink and downlink
Uplink
  600 Hz bandwidth, 600 bps, DBPSK
Downlink
  1.5 kHz bandwidth, 600 bps, GFSK
Particularly optimized for Europe
  Uplink on 1% duty cycle channel, up to 14 dBm
  Downlink on 10% duty cycle channel, up to 27 dBm
Works fine in US too
  Gets more power (24 dBm up is typical, up to 32 dBm down) and more range

## Slide 40: Sigfox link budget
Why transmit at 100-600 bps?
  For greatly increased link budget
Link budget: 150-160 dBm
  Assuming Tx at ~20 dBm
  Means Rx Sensitivity of -130 dBm (10 dBm better than LoRaWAN)
Resulting range: 10-15 km in urban environments
  Except that buildings lead to dead spots in range

## Slide 41: Sigfox MAC
Aloha-style access control (send whenever)
  No acknowledgements!
Send message three times for increased reliability
  Then listen for downlink at a set period later on a known frequency

## Slide 42: Sigfox deployments
Proprietary network with managed deployment
  Like cellular networks
  Sigfox deploys networks and transports data
  140 uplink messages plus 4 downlink message per day
Connectionless communication
  Devices are registered with the networks
  Keys are provided in the software image
  Any deployed Sigfox gateway can collect transmitted data
    Enables mobile applications

## Slide 43: IEEE standard for LPWANs
802.11ah (HaLow) standard in 2016
  First real hardware in 2020
  Still not in real-world use yet
Focus on the indoor-to-outdoor scenario
  Medium range (maximum 1 km)
915 MHz communication
  NOT interoperable with other 802.11 access points and devices
Theoretically up to 356 Mbps
  Practically, most devices are expected to implement 150 kbps to 8 Mbps
n.b.
802 = “area networking”
.3 = “LANs”
.11 = “Wireless LANs”
.15 = “PANs”

## Slide 44: 802.11ah allows multiple bandwidth allocations

## Slide 45: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Routing Basics
Flooding
Reactive and Proactive routing

## Slide 46
Routing

## Slide 47: What do you mean by routing?
You know destination, have a packet, how do you send this packet towards the destination node ? This is the routing question.
Routing is trivial if all nodes are connected to each other
Problem: if N nodes, need N(N-1) or O(N2) (uni-directional) links
  Simple techniques: broadcast, tree structures
  Mesh techniques: understand available routes and select a “good” one

## Slide 48: Performing routing in the wired networks
Number of links can be reduced very significantly with one “BIG” switch with N links and routing is still simple
Problem: If N is large and nodes can be far apart (think of the Internet)
Adding more switches/routers would reduce the size of the switches/routers needed and allow network to grow
  Think Internet!
But Routing will be more complex!

## Slide 49: Performing routing in the wireless networks
Routing protocols are complex, hard to maintain/debug and incurred significant overhead. More so for wireless networks.
In practice, wireless network deployments are single-hop and routing is trivial. All stations/devices communicating directly with base stations
  Example: WiFi, Cellular Network, LoRa
  Can one-hop communication be always sufficient by using sufficiently long range radio and large number of base stations?
Why multi-hop routing?
  Better in terms of reach/coverage for the same number of base stations
  Provides more routes, potentially more robust

## Slide 50: For the same distance, is it better to have direct or multi-hop path?
A
B
A
D
C
B
E
Which option is better?
Typically, a single-hop is considered better

## Slide 51: But, for energy Consumption …
Is multiple-hop transmission more energy efficient than a single-hop ?
Let us Recall the free space model: Pr = C Pt / da (C = constant)
Transmission over a distance d, let minimum received power needed be P0
  1 transmission to cover distance d, transmission power (P1) needed is
    P0 = C P1 / da or P1 = P0/C * da
  N transmissions to cover distance d, transmission power needed (PN) per hop is
    P0 = C PN / (d/N)a , or PN = P0 /C * (d/N)a
    Total transmission power is N PN = N P0 /C * (d/N)a
Which approach (1 transmission vs N transmissions) is more energy efficient?

## Slide 52: What are the simplest routing solutions?
Broadcast
  The link-layer solution for everything
Star topology
  Only one location to send to: parent
  Single parent needs to store information about all children
    Addresses, schedules, etc.
Tree topology
  Two choices: send to descendent or send to parent
  Each parent needs to store information about all children beneath it

## Slide 53: Many-to-one routing
Tree optimization for sensor networks
  Keep all devices except the “gateway” as simple as possible
Each device only needs to remember hop to gateway
  If gateway wants to send message back, it must include a full hop path

## Slide 54: Mesh Routing
Formed by a network of static wireless nodes
Mesh topology makes routing question more complicated
  Multiple hops in a route
  Multiple routes between source and destination
  Becomes a graph theory question based on cost metric
A
B
C
D
E
F

## Slide 55: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Routing Basics
Flooding
Reactive and Proactive routing

## Slide 56: What is the mesh equivalent of broadcast?
Flooding is the mesh equivalent of broadcast (communicate to all)
  Each node sends information to every other node in the mesh
  Eventually the packets will reach the desired destination
Goal: get information to all nodes
  This is the problem of “data dissemination”
Problem: difficult in Mesh topologies
  Packet loss, retransmission delays
Question: How do we make flooding stop?
Question: Is it really routing?

## Slide 57: What is the mesh equivalent of broadcast?
Flooding is the mesh equivalent of broadcast (communicate to all)
  Each node sends information to every other node in the mesh
  Eventually the packets will reach the desired destination
Goal: get information to all nodes
  This is the problem of “data dissemination”
Problem: difficult in Mesh topologies
  Packet loss, retransmission delays
Question: How do we make flooding stop?
Question: Is it really routing?

## Slide 58: What is the mesh equivalent of broadcast?
Flooding is the mesh equivalent of broadcast (communicate to all)
  Each node sends information to every other node in the mesh
  Eventually the packets will reach the desired destination
Question: How do we make flooding stop?
  Maximum retransmissions counter on each packet
    Decrement at each hop. Drop packet when it hits zero
    Need some guess for how many hops to destination
  Keep some history of recently flooded packets
    Don’t retransmit a recently sent packet
Question: Is it really routing?

## Slide 59: Glossy: what if we expand broadcast range by having multiple nodes participate?

## Slide 60: Glossy key techniques
Temporally decouple network flooding from application tasks
Exploit synchronous transmissions for fast network flooding

## Slide 61: Synchronous transmissions
Multiple nodes transmit same packet at same time
R can receive packet with high probability if Δ is small
  May even improve probability of reception (more energy at receiver)
500 ns is 1/32 of a symbol for 802.15.4 (chip duration)

## Slide 62: Fast packet propagation in Glossy

## Slide 63: Fast packet propagation in Glossy

## Slide 64: Fast packet propagation in Glossy

## Slide 65: Fast packet propagation in Glossy

## Slide 66: Glossy details
When Glossy starts
  All nodes turn on radios to receive

## Slide 67: Glossy details
Initiator
  Set relay counter in packet, C = 0
  Broadcast packet

## Slide 68: Glossy details
At packet reception:
  Increment relay counter C
  Transmit synchronously (at a fixed period after the reception)

## Slide 69: Glossy details
At packet reception:
  Increment relay counter C
  Transmit synchronously (at a fixed period after the reception)

## Slide 70: Glossy details
Stop rebroadcasting and turn off radio when
  Already transmitted N times
  Networks pick N for reliability/energy tradeoff

## Slide 71: Glossy details
Tslot is constant by design
  Needs to be to make constructive interference work
Beginning of slot (tref) provides synchronization point
  As a bonus, all nodes are synchronized after flooding event

## Slide 72: Glossy implementation
Device must be able to have tight time bounds on rx/tx
  500 ns wiggle room maximum
  Includes receive, processing, transmission
Need to pick an N for reliability

## Slide 73: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Routing Basics
Flooding
Reactive and Proactive routing

## Slide 74: Routing in wireless mesh and routing metrics
What are some possible metric to make routing decisions?
Hop Count
Delay
Reliability
Energy
Other?

## Slide 75: Reliability as a cost metric
Link quality can very from node to node
  Fewest hops might not be the “fastest” or “most reliable” path
ETX: minimize “expected transmissions”
  Measure link quality over time to determine each link’s reliability
A
B
C
D
E
F

## Slide 76: Routing metrics for internet of things
Some important consideration: low-power, energy efficiency, duty cycled operations of the radio transceivers
Each device needs to decide if a link (to another node) is available
How can this decision be made?
  Usually through some form of measurements
  A node sends beacon and other nodes check if the beacon can be received

## Slide 77: Low-power wireless links: PRR, RSSI
PRR – Packet Reception Ratio
RSSI – Received Signal Strength Indicator
Kannan Srinivasan and Philip Levis, “RSSI is Under Appreciated,” EmNets 2006.

## Slide 78: Measuring Low-Power Wireless Link Quality
To measure PRR,
  Receiver assumes that a transmitter sends S packets over a period of time T sec
  In T sec, record the number of packets received from transmitter, let this be R
  PRR = R/S
Example:
  T = 1sec, S=100 (if R=95, PRR=0.95)
  T= 10sec, S=100 (if R=55, PRR=0.55)
  T= 100s, S=10 (if R=8, PRR=0.8)

## Slide 79: Measuring Low-Power Wireless Link Quality
Trade-off between communication cost and reaction time
Assume ZigBee radio is used (250Kbps), each transmission takes 1ms (~250bits, ~30bytes) and link measurement probes should not collide
If T=1s, S=100
  Measurement takes up 10% of bandwidth 1 node
  If there are 10 nodes, 100 probes need to be transmitted in 1 sec (100% of bandwidth used only for measurement!)
If T=100s, S=10
  Measurement takes up very little bandwidth
  Is S too small?
  If there is a change in link quality, how long does it take to notice?
    What are “good” values for T and S?

## Slide 80: Who are my neighbors?
In order to reduce memory and computation cost, neighbor table tends to be small (e.g. 6 – 10)
  How many neighbors are sufficient?
  Only keep track of “good” neighbors

## Slide 81: Who are my neighbors?
Possibility of network partition
  Links within each room is good
  The one link between the 2 room is weak
  If all nodes select the best links, there will be no connection between rooms 1 and 2
Room 1
Room 2

## Slide 82: Expected number of transmissions: ETX
ETX (expected transmissions) is a commonly used routing metric
Consider the path A -> B -> C
Packet reception ratio (PRR)
  A -> B is 0.8, ETX = 1/0.8 = 5/4
  B -> C is 0.5, ETX = 1/0.5 = 2
  Path ETX (A -> B -> C) is 5/4 + 2 = 13/4
A
B
C

## Slide 83: Performing routing using the shortest path
Many practical routing algorithms are based on the notion of shortest path between two nodes
  Each link is assigned a positive number called its length
  A shortest path routing algorithm routes each packet along the minimum length (or shortest) path between the source and destination
  If length is always 1, then shortest path becomes minimum hop routing
  By defining the length using other metrics like cost, delay etc, other paths can be obtained

## Slide 84: Classification of the routing protocols
The existing routing protocols can be classified as:
Proactive: When a packet needs to be forwarded, the route is known
Reactive: Determine a route only when there is data to send

## Slide 85: Reactive routing
Build up a map of the routes through a network
  Hopefully the “optimal” routes
Map routes in reaction to a packet arrival
  Sensor devices are slow and limited
  Most likely to resend to same prior address
  Discover a route when it is needed, then cache for next time

## Slide 86: Distance-Vector
Keep routes as “next hops” rather than full routes
  AODV uses this method (DV for Distance Vector)
Can be combined with proactive techniques too
  Each router periodically informs neighbors of its shortest paths to each destination (in terms of hop count)
  Routers choose the best route available
    Old next-hop it was already aware of
    New next-hop through neighbor (with cost of their hops + 1)

## Slide 87: Ad-hoc On-demand Distance Vector Routing (AODV)
On-demand: Construct routes only when needed
Routing table
  Destination node -> Next hop
  Store only next hop instead of full route
    All routers along the path must also have Destination->Next mappings
  Also keep hops-to-destination and last-seen-destination-sequence-number
Route discovery
  Upon demand: check table
  If not cached send Route Request (RREQ) via Flooding
    Route is unknown, so flooding is needed

## Slide 88: AODV Route Requests (RREQs)
Request ID identifies this RREQ
  Used to discard duplicates during flooding
Sequence Numbers are per-device, monotonically increasing
  Used as a notion of “how recently” device has been seen
  Source SeqNo is the source’s most recent sequence number
  Destination SeqNo is the most recently seen from the destination by the source. (Defaults to zero)
Hop Count is the number of hops this request has taken
  Starts at 1 and incremented by each transmitter along the path
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count

## Slide 89: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
A wants to find a route to F, so it sends out an RREQ

## Slide 90: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 1
B and D also opportunistically add a routing table entry for A

## Slide 91: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 2
B goes first via some access control protocol (D also in contention)
A and D ignore duplicate Request ID C opportunistically adds a routing table entry to A

## Slide 92: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 2
D goes next by some access control protocol (C also in contention)
A, B, and C ignore duplicate Request ID E and F opportunistically adds a routing table entry to A

## Slide 93: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 3
C and E repeat this process with Hop Count 3 (but everyone ignores them)

## Slide 94: AODV Route Response (RREP)
Reply is sent unicast back to the source via newly constructed route
  Each node along the way already knows the route back
Includes recent destination sequence number as a sense of recency
  No need for source sequence number anymore
Source Address | Destination Address | Destination SeqNo | Hop Count

## Slide 95: Example AODV RREP (F to A)
A
B
C
D
E
F
Source Address | Destination Address | Destination SeqNo | Hop Count
F | A | 7 | 2
F sends response back to A via D
D opportunistically adds a routing table entry for F

## Slide 96: Route maintenance in AODV
If a link in the routing table breaks, all active neighbors are informed with Route Error (RERR) messages
  After some number of retransmissions and timeouts
  RERR contains destination address that broke
Nodes receiving RERR can start RERQ for destination address
  Which lets them find a new path through the network
  And updates everyone’s cached next-hops

## Slide 97: Tradeoffs for reactive routing
Upside: no transmissions unless there is demand
  Routes might appear, disappear, reappear, but no need to update if no one actually wants to transmit anything
Downside: large, variable delay when actually sending a packet
  Full RREQ/RREP protocol before data can actually be sent
  Route might have broken at some point
    So data will be sent based on cached information
    RERR will occur
    RREQ/RREP will occur
    Then data will be sent again

## Slide 98: Proactive routing
Alternative to reactive is to know the routes ahead of time
Periodically query for the possible routes in the network
  Save all routes that are important (maybe just all routes?)
  Also redetermine routes whenever topology changes (nodes join/leave)
Upside: when a packet arrives, route to destination is already known
Downside: requires more memory and effort on part of routers
  Wastes some network bandwidth on checking for route changes

## Slide 99
RPL

## Slide 100: Routing Protocol for Low Power and Lossy Networks (RPL)
● Distance Vector (DV) protocol
  Requires that a router to inform its neighbors of topology changes periodically
  Each node maintains a vector (table) of minimum distance to every node
● Source Routing Protocol
  Allows a sender of a packet to partially or completely specify the route the packet takes through the network

## Slide 101: Routing Protocol for Low Power and Lossy Networks (RPL)
(Directed Acyclic Graph)

## Slide 102: Routing Protocol for Low Power and Lossy Networks (RPL)

## Slide 103: Routing Protocol for Low Power and Lossy Networks (RPL)

## Slide 104: RPL: Control Messages
DODAG Information Solicitation (DIS): used to solicit a DODAG Information Object from a RPL node.
DODAG Information Object (DIO) - The DODAG Information Object carries information allows a node to discover a RPL Instance, learn its configuration parameters, select a DODAG parent set, and maintain DODAG
  RPL nodes transmit DIOs using a Trickle Timer.
Destination Advertisement Object (DAO): The Destination Advertisement Object (DAO) propagates destination information Upward along the DODAG.
DAO-ACK

## Slide 105: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Routing Basics
Flooding
Reactive and Proactive routing

## Slide 106: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.