## Slide 1: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.

## Slide 2: Discussion regarding Assignment 2
Assignment 2: Deadline 18th March
Submission after deadline: Penalty of 10% Per Day (until 24th March)
Submission link is now available on the Canvas
Please submit a readme file, source code, statement of work and a video demonstrating the operation of the sensor tag. The statement of work should describe the contribution made by every member of the group. You need to submit the source code for Task 2 and Task 3 as separate files. Only one member should submit the assignment on the canvas.
Notes: ++ We may all have heard of the term Internet of Things. So how are these wireless embedded systems related to the Internet of Things: Today, IoT includes a broad class of devices, including powerful platforms such as smartphones. However, it also includes more resource-constrained devices and what we call Wireless Embedded Systems, and in fact, I consider it to be one of the essential parts of the IoT ecosystem.
++ These are platforms equipped with a radio transceiver, sensor, microcontroller, and some form of energy storage. These platforms also often form a network, and sensor network as it is called has been an active area of research for the past two decades.
++ The research community has also developed wireless embedded platforms which we may know about, and these include: CMUCAM, which is an image sensor platform developed at Carnegie Mellon University, or Permamote is long life sensor platform from the lab I am associated with at UC Berkeley or Lorea which is a long-range backscatter platform that I had developed as part of my doctoral dissertation at Uppsala University. All of these are an example of Wireless Embedded Systems.

## Slide 3: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Communication layers and need for medium access control
MAC: Channelization protocols
MAC: Random access protocols
Medium access control for internet of things
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 4
Let us review the last lecture

## Slide 5: One way to understand backscatter mechanism
Notes: It can be thought of as a wireless equivalent of reflecting light using a mirror.

## Slide 6: Backscatter transmits at (up to) 10000x lower power consumption than conventional radios
Backscatter through absorption or reflection of ambient wireless signals enables wireless transmissions at microwatts of power consumption
RF Switch
Modulating Signal (Digital)
Antenna
Backscatter tag
Ambient RF signal
Reflected (backscatter) signal
Receiver
Notes: Backscatter communication actually help us overcome this limitation

## Slide 7: Backscatter is not a new transmission mechanism
First backscatter system: Great seal bug (The Thing) 1945
RFIDs: one of the most widely deployed backscatter system
Great Seal Bug (Backscatter device embedded for spying)
RFID System

## Slide 8: RFID is everywhere nowadays
Fundamental design principle is asymmetry
  Extremely simple, cheap tags
  Complex readers

## Slide 9: Radio Frequency ID
Cheap, low-power ubiquitous communication
  RFID tags on (or in) products
  NFC communication to/from smartphone
Requirements
  Need to transmit small amount of data (ID)
  Need to operate with little or no energy
    Most do not have batteries
  Short interaction time (fast enough bit rate)
  Range can be extremely limited
    Meters to centimeters (or millimeters)

## Slide 10: LoRea bridges the energy asymmetry between communication (TX), sensing and processing
Off-the-shelf hardware for transmission and receptions. Tens of USD
Overturn notion that backscatter is a short-range transmission mechanism
Backscatter Tag Hardware Prototype
(Peak Power of 70 µW)
Texas Instruments CC1310 Launchpad: Receiver
Component | Power Consumption
LoRea (Transmissions) | 70 µW (868 MHz)
Conventional Transceiver | Tens to hundreds of mW’s
Microcontroller (Apollo3) | 100s of µW’s
Sensors | Few to tens of µW’s
LoRea transmits at similar power consumption as a sensor
Notes: + Thus, with LoRea, we were able to design a backscatter system that was able to overcome the range and cost limitations that had limited all the existing backscatter system, and had hindered the widespread usage of the mechanism on the IoT devices
.
+ In fact, the backscatter tag even though it was designed using off-the-shelf components is orders of magnitude more efficient than commercial transceivers while supporting orders of magnitude lower power consumption.
+ the entire backscatter setup costs just few tens of USDs, which dramatically lowers the cost of infrastructure required to support the backscatter tags and carrier emitter device.

## Slide 11: What is the expected lifespan of a battery?
Coin cell (CR2032): 240 mAh, Flexible battery (Molex): 10 mAh
Backscatter transmitter: (LoRea, SENSYS 2017) – 35 uA
Let’s estimate long would battery last under different device load:
Component | Current draw | Flexible Battery | Coin cell
Microcontroller | 200 uA | 50 h | 1200 h
Accelerometer | 10 uA | 1000 h | 24000
WiFi Transmitter | 15 mA | 45 mins | 16 h
Bluetooth Transmitter | 1 mA | 10 h | 240 h
Backscatter Transmitter | 35 uA | 285.7 h | 6857 h

## Slide 12: What's next? Embedded systems on harvested energy
𝜇W
Energy harvester
Microwatts of power available to harvest from ambient sources
Notes: ++ The high-power consumption for the IoT platforms also blocks an important and promising direction to enable the sustainable deployment of large-scale embedded devices. This is to eliminate batteries from these platforms altogether. If we eliminate batteries, how do we power these devices?
++We use the fact that ambient energy sources surround us. We are constantly bombarded with radio frequency transmissions such as television, wifi, radio signals, or we have waste heat energy sources, or the indoor light is ubiquitous. All these sources could be harvested to derive energy to power the IoT devices and platforms and eliminate the overhead associated with batteries on these platforms. However, the challenge that we encounter is that we could only derive microwatts of power from these ambient sources, which is sufficient to power the sensors and microcontrollers. However, we need orders of magnitude higher power for operating radio transceivers such as LoRa. This makes it challenging, if not impossible, to power sensors through energy derived from the environment.

## Slide 13: Embedded systems on harvested energy
Batteries/Capacitors can potentially be recharged by environmental effects
Some examples
  Solar : solar cell
  Wind: micro wind turbine can be used to harvest wind energy readily available in the environment in the form of kinetic
  Thermal: capture energy from industrial equipment, structures, and even the human body.
  Vibration: vibration from engines can stimulate piezoelectric materials, as can the heel of a shoe.
  Kinetic: translate movement to change in electromagnetic flux
  Radio Frequency (RF): convert ambient RF signal into energy (demo video)

## Slide 14: What communication modality do these use?

## Slide 15: Communication using inductive coupling
A shared magnetic field is created between the two devices
  Change in current through one device induces current change through the other
  Device can vary load to transmit data
Very low frequency bands (135 KHz, 13.56 MHz)
  Transmit through materials including skin
  Sensitive to metal

## Slide 16: Near Field Communication (NFC)
Inductive Coupling concept (13.56 MHz)
  But attached to a powered and capable device (smartphone)
  10-20 cm range max (usually <10)
Can act as a tag or as a reader
  Allows smartphone to power a tag if needed
  Alternatively, smartphone could act like a card and respond to a reader
  Two smartphones can communicate without power transfer
Data rate 100-400 kbps!
  nRF52840 capable of 100 kbps communication with attached antenna

## Slide 17: Light Fidelity (LiFi) for Internet of Things
Illumination
Energy
Communication
00100111
0
1
0
0
0
1
1
1
Advantages:
Light-fidelity
Notes: Let’s start the background story from LiFi
Light fidelity is a wireless technology that uses visible light for data transmission. The information is modulated on the light signal according to the baseband signal.
LiFi offers advantages, such as using a different part of the specturm other than crowded RF electromagnetic signal
In addtion, it simultaneously provide, illumination, energy and communication
Which makes it a good candidate for IoT connectivity.

## Slide 18: LiFi communication suffers from coverage challenges
Light cannot propagate through walls or other such physical boundaries
  Great from privacy perspective, but limits deployable location of IoT devices
Many IoT devices are located in places with very poor light propagation
  IoT devices that are located in the air vents
  Inside the wall, floor and other surfaces
  IoT devices that are embedded inside the human body
Notes: Light signal can not propagate through physical spaces. Things like walls, floors, metals block light signal.
When considering privacy, this is an advantage. However for IoT applications, it limits the scenarios where sensors located in places with poor light propagation.

## Slide 19: Example of LiFi communication from a collaborator
Notes: Light signal can not propagate through physical spaces. Things like walls, floors, metals block light signal.
When considering privacy, this is an advantage. However for IoT applications, it limits the scenarios where sensors located in places with poor light propagation.

## Slide 20: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Communication layers and need for medium access control
MAC: Channelization protocols
MAC: Random access protocols
Medium access control for internet of things
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 21
Communication Layers
Notes: ++ Over the past few years, I have designed several backscatter and beyond backscatter systems that precisely overcome these critical challenges that have limited the widespread deployment of backscatter on IoT devices.
++ The research vision that I have pursued and would like to pursue as a faculty member is to enable a massive deployment of IoT devices by bridging the energy asymmetry between sensing, computation and communication blocks by designing novel platforms and communication mechanisms. I am going to describe some of my research contributions next.

## Slide 22: OSI model of communication layers
Transport
  How to form connections between computers
  TCP and UDP
Network
  How to send packets between networks
  IP
Data Link
  How to send frames of data
  Ethernet, WiFi
Physical
  How to send individual bits
  Ethernet, WiFi

## Slide 23: Protocols are “layered”
Headers for each layer of communication wraps data
  Data is wrapped with header for the network to make a packet
  Packet is wrapped with header for the link to make a frame
Data
Packet Header
Frame Header
Internet Packet
Ethernet Frame

## Slide 24: Data Link Layer
Framing
  Combine arbitrary bits into a “packet” of data
Logical link control
  Manage transfer between transmitter and receiver
  Error detection and correction
Media access
  Controlling which device gets to transmit next
Inherently coupled to PHY and its decisions

## Slide 25: Framing
Typical packet structure
  Preamble - Existence of packet and synchronization of clocks
  Header - Addresses, Type, Length
  Data - Payload plus higher layer headers (e.g. IP packet)
  Trailer - Padding, CRC
Wireless considerations
  Control information for Physical Layer
  Ensure robustness for header
  Explicit multi-hop routing
  Possibly different data rates for different parts of packet
Preamble | Destination Address | Source Address | Type and Length | Data | CRC

## Slide 26: Error control: detection and recovery
Detection: only detect errors
  Make sure corrupted packets get discarded
  Cyclical Redundancy Checks
    Detect single bit errors
    Detect “burst” errors of several contiguous bits
Recovery: also try to recover from small bit errors
  Forward error correction
  Retransmissions
  Far more important for wireless because the cost of transmission is higher

## Slide 27
Need for Medium Access Control
Notes: ++ Over the past few years, I have designed several backscatter and beyond backscatter systems that precisely overcome these critical challenges that have limited the widespread deployment of backscatter on IoT devices.
++ The research vision that I have pursued and would like to pursue as a faculty member is to enable a massive deployment of IoT devices by bridging the energy asymmetry between sensing, computation and communication blocks by designing novel platforms and communication mechanisms. I am going to describe some of my research contributions next.

## Slide 28: What is hard about wireless?
There are no wires!
Wired networks are constant, reliable, and physically isolated
  Ethernet has the same throughput minute-to-minute
  Bits sent through Ethernet or USB are (usually) received
Wireless networks are variable, error-prone, and shared
  WiFi throughput changes based on location and walls
  Signals from nearby devices interfere with your signals
  Individual bits might flip or never be heard at all

## Slide 29: Wireless is a shared medium
Wired communication has signals confined to a conductor
  Copper or fiber
  Guides energy to destination
  Protects signal from interference
Wireless communication is inherently broadcast in nature
  Energy is distributed in space
  Signals must compete with other signals in same frequency band

## Slide 30: Increasing network capacity is challenging
Wired networks just add more wires
  Buses are many signals in parallel to send more data
Wireless networks are harder
  Adding more links increases interference
  Need to expand to different frequencies

## Slide 31: Wired vs. Wireless
Key difference between wired and wireless is the need to support multiple access as wireless is broadcast in nature
How does a network determine which transmitter gets to transmit?
Remember: the wireless medium is inherently broadcast
  Two simultaneous transmitters may lose both packets

## Slide 32: Analogy: wireless medium as acoustic
How do we determine who gets to speak?
  Two simultaneous speakers also lose both “transmissions”
Eye contact (or raise hand) -> out-of-band communication
Wait until it’s quiet for some time -> carrier sense multiple access
Strict turn order -> time division multiple access
Just speak and hope it works -> ALOHA
Everybody sing at different tones -> frequency division multiple access (stretching the metaphor)

## Slide 33: Wireless: What are challenges of multiple access
Problem: Multiple radio transmitters want to access a common channel
  How to coordinate access for these radio transmitters ?

## Slide 34: What can be mechanisms for multiple access
How to enable multiple devices to communicate over shared channel?
  Avoid or reduce collisions
  Detect collisions (less common in wireless)
  Decide when to retransmit

## Slide 35
Taxonomy of multiple-access protocols
Reduce collision,
“manage” retransmission
Avoid collision

## Slide 36: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Communication layers and need for medium access control
MAC: Channelization protocols
MAC: Random access protocols
Medium access control for internet of things
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 37
Channelization Protocols

## Slide 38: FDMA – Frequency Division Multiple Access
Separate transmissions by placing them at different frequencies
Channel:
Technically, each device can use a separate, fixed frequency
  One example can be walkie-talkies
  What are disadvantages of giving every device own frequency?
Conceptually, how RF channels work
  WiFi networks pick different bands
  802.15.4 picks a channel to communicate on

## Slide 39: FDMA – Frequency Division Multiple Access
Separate wireless transmissions by placing them at different frequencies
Channel:
Technically, each device can use a separate, fixed frequency
  One example can be walkie-talkies (mostly separate)
  What are disadvantages of giving every device own frequency?

## Slide 40: Wireless communication over multiple channels
Why do we need multiple channel for wireless communication?
  Increase throughput
  spatial diversity
  Increase reliability

## Slide 41: Multi Channel MAC Protocols
Use a control channel:
  Use of a default channel and time synchronization for control message exchange
  Nodes switch to a different channel for data communication
All channels are used for data communication:
  Nodes switches to another channel when link quality is bad
  How do we find a “good” channel to switch to?

## Slide 42: Wifi Channels
14 channels designated in the 2.4 GHz range spaced 5 MHz apart (with the exception of a 12 MHz spacing before channel 14)
https://en.wikipedia.org/wiki/List_of_WLAN_channels

## Slide 43: ZigBee Channels

## Slide 44: TDMA – Time Division Multiple Access
Split transmissions in time
  Devices share the same channel
Splits time into fixed-length windows
  Each device is assigned one or more windows
  Can build a priority system here with uneven split among devices
Requires synchronization between devices
  Often devices must listen periodically to resynchronize
  Less efficient use of slots reduce synchronization
    Large guard windows. E.g. 1.5 second slot for a 1 second transmission

## Slide 45: TDMA: Time Division Multiple Access‏
Consider a 1Mbps channel (1,000,000bits/sec)
Divide channel into 1000 (equal) times slots
Each slot is 1ms, and can transmit 1,000 bits
Assign slots to 50 users
  Each user transmits every 50 slots/ms and transmit 20 times/slots per second
  On average, each user can transmit 20kbps
Buffering is needed on both sender and receiver to match the differences in data rates
  sender-side: 20kbps -> 1 Mbps
  Receiver-side: 1Mbps -> 20kbps
Notes: 45
45

## Slide 46: TDMA vs. FDMA
Time
Frequency
In practical systems, TDMA is often combined with FDMA
Frequency
Time
FDMA
Time
Frequency
TDMA
Notes: 46
46

## Slide 47: Orthogonal Frequency Division Multiplexing :OFDM
In FDM, the entire frequency spectrum is dedicated to carry data from a single source
  Example: transmit at 40Mbps over a 20 MHz spectrum
In OFDM, data is divided into many (slower) bit streams and multiple subcarriers (each with smaller spectrum) is used
  Example: divide data source into 40 sources, each 1Mbps

## Slide 48: TSCH Network
Time is divided into slots, multiple slots form a slotframe
Sends to receiver on slots it is listening on (e.g. green to C, red to A)
Frequency chosen for a timeslot is based on a pseudo-random pattern
Scheduling policy is not standardized

## Slide 49: Frequency and Time leads to Spread Spectrum (SS)
Spread-spectrum techniques are methods by which a signal is deliberately spread in the frequency domain, resulting in a signal with a wider bandwidth
Such techniques can be used to establish secure communications, increase resistance to natural interference, jamming and to prevent detection
Concept has been alluded to in 1900s, and applied in some form during WWII
Resistant to narrowband interference
Signals are difficult to interpret – appears as if increase in background noise
Can share frequency band with others with minimal interference

## Slide 50: Spread spectrum: Frequency Hopping (FH)
FHSS increase resistance to a) natural interference b) jamming c) detection

## Slide 51: Spread spectrum: Frequency Hopping (FH)
A protocol that we use everyday uses Frequency hopping spread spectrum technique?

## Slide 52: Spread spectrum: Frequency Hopping (FH)
A protocol that we use everyday uses Frequency hopping spread spectrum technique?
Bluetooth hops between 79 different 1 MHz channels in the band.

## Slide 53: WiFi Channel Usage

## Slide 54: Cross Channel Interference (CTI)
A. Hithnawi, et.al.,TIIM: Technology-Independent Interference Mitigation for Low-power Wireless Networks, IPSN 2015

## Slide 55
Break! (5 minutes)
Notes: ++ Over the past few years, I have designed several backscatter and beyond backscatter systems that precisely overcome these critical challenges that have limited the widespread deployment of backscatter on IoT devices.
++ The research vision that I have pursued and would like to pursue as a faculty member is to enable a massive deployment of IoT devices by bridging the energy asymmetry between sensing, computation and communication blocks by designing novel platforms and communication mechanisms. I am going to describe some of my research contributions next.

## Slide 56: Farmbeats (TV Whitespace) (Courtesy: Microsoft)

## Slide 57: One of the last year’s question
Question: You are deploying IoT devices in farms to help increase agricultural yield. These IoT devices would monitor soil humidity and temperature, and then transmit this sensor information to a base station that is deployed in the center of the field. The base station is located several hundred meters away from the IoT devices. In this deployment, you plan to use TV whitespace for communication. You can assume that there is no synchronization between IoT devices. Television stations operate at frequency between 500 to 700 MHz.

## Slide 58: One of the last year’s question
Television Station | Frequency band
A | 500-508 MHz
B | 520-528 MHz
C | 540-548 MHz
D | 560-568 MHz
E | 580-588 MHz
Reserved | 620 MHz onwards
What are the frequency bands that are available for communication with the IoT device? (2 point)

## Slide 59: One of the last year’s question
Television Station | Frequency band
A | 500-508 MHz
B | 520-528 MHz
C | 540-548 MHz
D | 560-568 MHz
E | 580-588 MHz
Reserved | 620 MHz onwards
What are the frequency bands that are available for communication with the IoT device? (2 point)
Answer: a)
508-520 MHz
528-540 MHz
548-560 MHz
568-580 MHz
588-620 MHz

## Slide 60: One of the last year’s question
Television Station | Frequency band
A | 500-508 MHz
B | 520-528 MHz
C | 540-548 MHz
D | 560-568 MHz
E | 580-588 MHz
Reserved | 620 MHz onwards
What are the frequency bands that are available for communication with the IoT device? (2 point)
Answer: a)
508-520 MHz
528-540 MHz
548-560 MHz
568-580 MHz
588-620 MHz

## Slide 61: One of the last year’s question
Television Station | Frequency band
A | 500-508 MHz
B | 520-528 MHz
C | 540-548 MHz
D | 560-568 MHz
E | 580-588 MHz
Reserved | 620 MHz onwards
b) If each of the IoT device requires 500 KHz of bandwidth for communication, how many such concurrently transmitting IoT devices can be supported at the base station? Please justify your answer and mention assumptions made while performing this calculation. (2 point)

## Slide 62: One of the last year’s question
Television Station | Frequency band
A | 500-508 MHz
B | 520-528 MHz
C | 540-548 MHz
D | 560-568 MHz
E | 580-588 MHz
Reserved | 620 MHz onwards
b) If each of the IoT device requires 500 KHz of bandwidth for communication, how many such concurrently transmitting IoT devices can be supported at the base station? Please justify your answer and mention assumptions made while performing this calculation. (2 point)
Available bandwidth = (520-508) + (540-528) + (560-548) + (580-568) + (620 - 588) = 12 + 12 + 12 + 12 + 32 = 80 MHz
Each IoT device requires 500 KHz of bandwidth.
Number of devices = Total available bandwidth / Bandwidth per device
= 80 MHz / 0.5 MHz = 160 devices
Assuming all devices operate in non-overlapping frequency bands, up to 160 concurrently transmitting IoT devices can be supported at the base station.

## Slide 63: One of the last year’s question
c) What would be the medium access control mechanism and modulation scheme that you would like to use in this deployment? (1 point)
d) If you were to design a custom protocol for communication between IoT devices and the base station, how would you structure the packet? Describe the various fields, their sizes, and any other relevant information. (1 point)

## Slide 64: One of the last year’s question
c) What would be the medium access control mechanism and modulation scheme that you would like to use in this deployment? (1 point)
d) If you were to design a custom protocol for communication between IoT devices and the base station, how would you structure the packet? Describe the various fields, their sizes, and any other relevant information. (1 point)
c) We would like to use modulation scheme that enables sufficiently large range at low power. Modulation scheme such as FSK, Lora with CSS. We would use simple medium access control mechanism such as Aloha.
One example:
Preamble (8 bits), Packet Length (8 bits), Device ID (16 bits), Timestamp (32 bits), Soil Humidity (16 bits), Soil Temperature (16 bits), Battery Level (8 bits), CRC (16 bits)

## Slide 65: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Communication layers and need for medium access control
MAC: Channelization protocols
MAC: Random access protocols
Medium access control for internet of things
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 66
Random Access Protocols

## Slide 67: Random access medium access control protocols
No coordination
The simplest: ALOHA
  When a node needs to send, it does so.
  If it hears an acknowledgment within a given duration, transmission is successful
  otherwise, it resends after waiting a random amount of time.
Protocol strength
  minimum overhear
  achieves low delay if the load is light

## Slide 68: ALOHA
ALOHAnet (1971)
  University of Hawaii – Norman Abramson
  First demonstration of wireless packet network
Rules
  If you have data to send, send it
Two (or more) simultaneous transmissions will collide and be lost
  Wait a duration of time for an acknowledgement
  If transmission was lost, try sending again “later”
    Want some kind of exponential backoff scheme here

## Slide 69: Packet collisions
Each packet transmission has a window of vulnerability
  Twice the on-air duration of a packet
  Transmissions during the packet are bad
  Transmissions before packet can also be bad

## Slide 70: Slotted ALOHA
Split time into synchronized “slots”
Any device can transmit whenever it has data
  But it must transmit at the start of a slot
  And its transmission cannot be longer than a slot
  Removes half of the possibilities for collisions!
    At the cost of some synchronization method
time

## Slide 71: ALOHA throughput
It can be shown that traffic maxes out at
  ALOHA: 18.4%
  Slotted ALOHA: 36.8%
Assuming Poisson distribution of transmission attempts
Slotted throughput is double because the “before” collisions can no longer occur

## Slide 72: Carrier Sense Multiple Access
Carrier Sense Multiple Access:
  sense carrier
  If idle,
    send
    wait for ack
    If there isn’t one, assume there was a collision, retransmit
Should we transmit immediately once channel is idle?

## Slide 73: Carrier Sense Multiple Access/ Collision Avoidance
CA – Collision Avoidance
if the channel is clear, deferred transmission for a "random" interval
  Choose interval from a uniform distribution with values between 0 and maximum window size Wmax
  reduces the probability of collisions on the channel
How large should Wmax be?
  If interval is long, time is “wasted” …
  If interval is too short?

## Slide 74: CSMA/CA: Choosing Wmax
Should Wmax be constant?
Intuitively, Wmax should be small when there is lower chance of collision and vice versa
Wmax varies according to the Binary Exponential Backoff (BEB) algorithm.
Set “slot time” to 2 times the max. propagation delay on the channel
    If this is the first transmission, sends immediately
    If there is a collision, after i-th collision, pick Wmax randomly between 0 and 2i-1 time slots.

## Slide 75: CSMA/CA: Trade-off
What are the Trade-off:
  More aggressive (smaller Wmax) – more likely to achieve higher channel utilization, but also more likely to collide
  Less aggressive – lower channel utilization, less likely to collide
Utilization vs. delay
  Overly aggressive or conservative can increase delay
Optimal point depends on
    Number of stations/nodes contenting
    Traffic load

## Slide 76: Window Size “Tuning”
Wmax window can be varied to change the share of the bandwidth that are allocated to various mobile nodes
Main idea: station/node with “smaller” Wmax gets larger share of bandwidth
  Problem: find the “right” combinations of window sizes for different nodes

## Slide 77: Hidden terminal problem
Device A
Device B
Device C

## Slide 78: CSMA with RTS/CTS
Hidden terminal problem means that two transmitters might never be able to detect each other’s transmissions
A partial solution
  When channel is idle, transmitter sends a short Request To Send (RTS)
  Receiver will send a Clear To Send (CTS) to only one node at a time
  RTS collisions are faster and less wasteful than hidden terminal collisions
  Downside: overhead is high for waiting for CTS when contention is low

## Slide 79: Solving Hidden Terminal Problem
A
B
C
RTS
CTS
CTS
OK, I’ll wait …

## Slide 80: Real-world protocol access control
ALOHA
  BLE advertisements
  Unlicensed LPWANs: Sigfox, LoRaWAN
CSMA
  WiFi (slotted, CSMA/CA)
TDMA
  BLE connections
  Cellular LPWANs: LTE-M and NB-IoT

## Slide 81: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Communication layers and need for medium access control
MAC: Channelization protocols
MAC: Random access protocols
Medium access control for internet of things
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 82
Medium Access Control for Internet of Things

## Slide 83: Medium access control for Internet of Things
Medium access control for normal wireless devices
  Low Latency
  High Utilization
  Fair (every has chance to communicate)
How about medium access control for internet of things?
  Power Consumption should be as small as possible
  (Most) sensor applications have low channel utilization
Designing medium access control with energy consideration as priority?

## Slide 84: Energy consumption of medium access control
The main sources of energy consumption in any contention-based MAC protocol:
  overhearing
  control packet overhead
  data transmission/reception
  idle listening
(1) – (3) occurs only when there is a transmission
(4) occurs even when there is no traffic

## Slide 85: “Life Cycle” of MAC Protocols
(4)
(1) – (3)
(4)
(1) – (3)
(4)
(1) – (3)
Less Traffic
(4)
(1 – (3)
(4)
(1) – (3)
Less Traffic
(4)
(4)

## Slide 86: Idle listening is energy expensive
Idle listening consumes most of the energy as traffic load decreases
Many measurements have shown that idle listening consumes 50–100% of the energy required for receiving
But if you do not listen to the channel, how do detect events/transmissions?

## Slide 87: Duty cycled medium access control protocols
Overhearing or passive listening is very expensive, in particular, if utilization is low
Proposal: Don’t overhear, go to sleep!
Advantage:
  Consume very little energy when radio is idle/inactive
Problem:
  When to wakeup?
Requirements:
  Wakeup schedule must be coordinated
  The “right” nodes must wake up at the “right” time

## Slide 88: Let's consider Aloha protocol
Consider the simplest MAC protocol – ALOHA
  No change to the protocol: when a node wants to transmit, it does
Does it work?
  Works when
    There is no contention (usually true when utilization is low)
    The receiver is listening (may not be true with duty cycle)
How to convert ALOHA to work with duty cycle?

## Slide 89: Aloha with Preamble Sampling
Preamble
Data
Sender
Receiver
Sensing
Sensing
Sensing
Sensing
Receiver 1
Sensing
Sensing
ACK
Recv
Receiver 2
Sensing
Sensing
(Possible we can miss the preamble and thus data?)
Sensing

## Slide 90: Aloha with Preamble Sampling
Each receiver periodically (every Tp) wakes up to check if the channel is busy for a duration of (Ts)
  If channel is busy, stays in listening mode until destination of data is known (transmitted), else go back to sleep for a period of (Tp-Ts)
Sender transmits a long preamble (Tp), and then send data packet at the end of the preamble period of packet transmission
Is this protocol energy efficient?
Preamble
Data
Sender
Receiver 1
Sensing
Sensing
ACK
Recv
Sensing
Tp
Ts
TD

## Slide 91: B-MAC: Asynchronous Medium Access Control
B-MAC asynchronous MAC protocol. Based on concept of preamble sampling
Nodes periodically activate their radios to detect signals; remain active upon receiving a packet or go to sleep after a set timeout if no activity is detected
To guarantee packet reception, the preamble duration must be at least as long as the channel sampling rate
Idle listening refers to when nodes check an inactive channel, resulting in unnecessary power usage
The preamble time (Tp) should align with the channel check interval for reception; for instance, a 100ms check requires a minimum 100ms preamble

## Slide 92: Improving B-MAC
While the design of B-MAC makes suitable for low power/low duty operations, its performance can be improved
Transmitter:
  Is a long (continuous) preamble necessary?
(Potential) Receivers:
  Is a long (average) waiting period necessary?

## Slide 93: Improving B-MAC with X-MAC
X-MAC improves over B-MAC
  Sender transmits many “probes” with gaps between probes. Each probe contains address of intended receiver
  Receiver checks address embedded in probe, sends acks if it is the destination during the gap period between probes
  Sender transmits DATA, receive replies with Ack to complete data transfer

## Slide 94: ContikiMAC
ContikiMAC is the MAC protocol implemented in Contiki OS

## Slide 95: Current draw for ContikiMAC

## Slide 96: Synchronous MAC
Why not let all nodes wakeup at the same time?
SMAC’s solution
  Some form of time division multiplexing
  Divide interval into listening and sleeping
  Percentage of listening period is the “duty cycle”

## Slide 97: Synchronous MAC (SMAC)
Example: 10% duty cycle
  Each node listens for 100ms and sleep for 0.9s
  Each node listens for 1s and sleeps for 9s

## Slide 98
Collisions are always bad?

## Slide 99: Receiving transmissions with collisions
Collision does not always lead to packet loss
If a receiver hears from two or more stations and the signal from one station is much stronger than the rest, the receiver can receive the signal correctly “only” from this station: This is called capture effect.

## Slide 100: Receiving transmissions with collisions
One receiver, multiple transmitters (transmit same packet)
With capture effect, adding new transmitters may improve reliability!

## Slide 101: Receiving transmissions with collisions
R
T2
-83.02dB
T1
-84.09dB
100%
35%
T3
-80.93dB
15%
T4
-70.89dB
99%

## Slide 102
Flooding

## Slide 103: Flooding is a recreation of broadcasts
Goal: get information to all nodes
  This is the problem of “data dissemination”
Problem: difficult in Mesh topologies
  Packet loss, retransmission delays
Really, data dissemination is just to broadcast to all nodes
  But broadcast transmissions don’t reach far enough to cover entire mesh

## Slide 104: Synchronous transmissions
Multiple nodes transmit same packet at same time
R can receive packet with high probability if Δ is small
  May even improve probability of reception (more energy at receiver)
500 ns is 1/32 of a symbol for 802.15.4 (chip duration)

## Slide 105: Fast packet propagation in Glossy

## Slide 106: Fast packet propagation in Glossy

## Slide 107: Fast packet propagation in Glossy

## Slide 108: Fast packet propagation in Glossy

## Slide 109: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Communication layers and need for medium access control
MAC: Channelization protocols
MAC: Random access protocols
Medium access control for internet of things
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 110: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.

## Slide 111: Google Project Loon? Do you know?
Google Project Loon: https://x.company/projects/loon/

## Slide 112: One of the last year’s question
Question: Over the past several years, we have seen a growing interest in utilizing satellites to provide wireless connectivity to Internet of Things (IoT) devices. These satellites usually operate at altitudes of 400 to 500 kilometers from the Earth's surface. However, this deployment of satellites has led to concerns regarding orbital congestion and pollution. As an alternative, high-altitude balloons are being explored to provide network connectivity to Internet of things devices. These balloons fly at much lower altitudes of around 20 kilometers from earth’s surface and they offer a very cost-effective solution to satellite launches.

## Slide 113: One of the last year’s question
If you are using low-altitude balloons to provide connectivity to ground based IoT devices. Please answer the following questions:
(a) What type of antennas are suitable for use on the high-altitude balloons and ground based IoT devices to ensure reliable communication? Provide appropriate rationale for your choice. (1 point)

## Slide 114: One of the last year’s question
If you are using low-altitude balloons to provide connectivity to ground based IoT devices. Please answer the following questions:
(a) Question: What type of antennas are suitable for use on the high-altitude balloons and ground based IoT devices to ensure reliable communication? Provide appropriate rationale for your choice. (1 point)
Balloon: We can use directional antenna such as parabolic antenna to ensure the energy is directed towards the deployment of IoT device.
On IoT devices: Omnidirectional antennas, as it can allow them to receive energy from any direction even if these devices are mobile. It would allow us to avoid positioning the nodes with limited line-of-sight to the balloon.

## Slide 115: Are these the only correct answers?
If you are using low-altitude balloons to provide connectivity to ground based IoT devices. Please answer the following questions:
(a) Question: What type of antennas are suitable for use on the high-altitude balloons and ground based IoT devices to ensure reliable communication? Provide appropriate rationale for your choice. (1 point)
Balloon: We can use directional antenna such as parabolic antenna to ensure the energy is directed towards the deployment of IoT device.
On IoT devices: Omnidirectional antennas, as it can allow them to receive energy from any direction even if these devices are mobile. It would allow us to avoid positioning the nodes with limited line-of-sight to the balloon.

## Slide 116: One of the last year’s question
If you are using low-altitude balloons to provide connectivity to ground based IoT devices. Please answer the following questions:
(b) Which frequency bands are suitable for communication between balloon and IoT device? Provide appropriate rationale for your choice. (1 point)

## Slide 117: One of the last year’s question
If you are using low-altitude balloons to provide connectivity to ground based IoT devices. Please answer the following questions:
(b) Which frequency bands are suitable for communication between balloon and IoT device? Provide appropriate rationale for your choice. (1 point)
Sub-GHz bands due to their superior propagation characteristics. Ideally, we should be looking at ISM frequency bands. For some application, perhaps, 2.4 GHz may also work.

## Slide 118: One of the last year’s question
(b) Which frequency bands are suitable for communication between balloon and IoT device? Provide appropriate rationale for your choice. (1 point)
Sub-GHz bands due to their superior propagation characteristics. Ideally, we should be looking at ISM frequency bands. For some application, perhaps, 2.4 GHz may also work.

## Slide 119: One of the last year’s question
(c) From a wireless communication perspective, what are two advantages and disadvantages of using balloons for connectivity in IoT devices compared to satellite-based solutions? (2 point)

## Slide 120: One of the last year’s question
(c) From a wireless communication perspective, what are two advantages and disadvantages of using balloons for connectivity in IoT devices compared to satellite-based solutions? (2 point)
There can be several advantages:
1. Lower latency owing to lower altitude of the balloon
2. We can use ISM frequency bands due to shorter distances for communication
3. Better signal quality owing to stronger signals
Cons:
1. Limited coverage when compared to satellites, may require several balloons overhead
2. Greater chance of interference with terrestrial and other such transmissions
3. Higher maintenance overhead to replace and maintain balloons

## Slide 121: One of the last year’s question
(d) Given that the IoT device is equipped with a radio with a receive sensitivity of -100 dBm and an antenna gain of 2 dB. There is an estimated distance of 20 kilometers between the balloon and the IoT device, and the balloon is equipped with 8 dB antenna. Please calculate the transmit power required at the balloon to ensure successful packet reception at IoT device. Use the frequency selected in part (b) for your calculations. The path loss exponent is 2. (4 point)

## Slide 122: One of the last year’s question
(d) Given that the IoT device is equipped with a radio with a receive sensitivity of -100 dBm and an antenna gain of 2 dB. There is an estimated distance of 20 kilometers between the balloon and the IoT device, and the balloon is equipped with 8 dB antenna. Please calculate the transmit power required at the balloon to ensure successful packet reception at IoT device. Use the frequency selected in part (b) for your calculations. The path loss exponent is 2. (4 point)
Homework (and tutorial question next week): We can use Friis propagation equation to estimate the answer. For 900 MHz, around 7 dBm transmitter strength.

## Slide 123: One of the last year’s question
(e) In a scenario where communication is limited to only transmission from the IoT device to the balloon, what kind of medium access control mechanism would be suitable for the IoT device? You can assume that IoT device is transmitting humidity and temperature readings. Provide appropriate rationale.

## Slide 124: One of the last year’s question
(e) In a scenario where communication is limited to only transmission from the IoT device to the balloon, what kind of medium access control mechanism would be suitable for the IoT device? You can assume that IoT device is transmitting humidity and temperature readings. Provide appropriate rationale.
Due to simplicity simple protocols like Aloha makes sense

## Slide 125: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.