## Slide 1: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.

## Slide 2: Administrative stuff
Course webpage: Canvas
First tutorial is already uploaded. Anyone without tutorial slot?
Ed: Platform for asking question, team mate. Received notification?
First lecture video is already uploaded on the canvas
Next week tutorial
  Missing session? Do on your own, and discuss with TA’s in the coming week
  Drop me a message and we can discuss tutorial as well

## Slide 3: Roadmap of the lecture today
Quick Recap
Antenna Continued
Line of Sight and Non Line of Sight
Modulation Basics

## Slide 4
Quick Recap
Notes: ++ Over the past few years, I have designed several backscatter and beyond backscatter systems that precisely overcome these critical challenges that have limited the widespread deployment of backscatter on IoT devices.
++ The research vision that I have pursued and would like to pursue as a faculty member is to enable a massive deployment of IoT devices by bridging the energy asymmetry between sensing, computation and communication blocks by designing novel platforms and communication mechanisms. I am going to describe some of my research contributions next.

## Slide 5: Trillion embedded devices will be deployed soon
1 per Enterprise
1 per Company
1 per Professional
1 per person
1 per Family
1 per Engineer
10’s per person
log (people per computer)
Mini Computer
Laptop
Workstation
Personal Computer
Mainframe
Smartphone
IoT/Wearable
100 – 1000’s per person
Smart Dust
“Roughly every decade a new, lower priced computer class forms based on a new programming platform, network, and interface resulting in new usage and the establishment of a new industry.”
[Bell et al. Computer, 1972, ACM, 2008]

## Slide 6: IC transistor count doubles every two years
Photo Credit: Intel
Notes: So if we look at the computing spectrum today, each of the classes exist simultaneously. In a room we can put 100s of teraflops and many petabytes of computing.
Our productivity, document preparation, and personal information management fits in our pocket and a new class is emerging that will provide a means of streaming information to and from the physical world like we have never seen before.

## Slide 7: MEMS Accelerometers: Rapidly falling price and power
[Analog Devices, 2009]
ADXL345
10 µA @ 10 Hz @ 6 bits
25 µA @ 25 Hz
Price
Power
[ST Microelectronics, annc. 2009]
O(mA)

## Slide 8: Fundamentals of electromagnetic waves
Electromagnetic (EM) waves are synchronized oscillations of electric and magnetic field. There is a periodic change of electric and magnetic field
How often this periodic change occurs dictates the property of EM waves
  Changer period is termed as the frequency. The SI unit for frequency is Hertz (Hz)
  1 Hz: one cycle of an electromagnetic wave in a second
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 9: What are radio transceivers?
Radio transceivers are components that enables the transmission and reception of electromagnetic waves. A key component in wireless device
Antenna
Transmitting
Device
Radio frequency signal
Receiving Device
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 10: How are radio waves characterized?
Radio waves can be characterized based on following parameters:
  Strength/Power: energy contained in the radio wave
  Frequency: rate of periodic variation between electric and magnetic field
  Bandwidth: range of frequencies of radio waves present in the transmission
  Polarization: orientation of electric field. May be circular, elliptical or linear
  Modulation: variation of waves property to encode information
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 11: How radio waves radiate out from transceiver
Antenna: An electrical conductor or system of conductors
  Transmission: radio frequency electrical energy converted into electromagnetic energy
  Reception: the reverse occurs, electromagnetic energy converted into electrical energy
Antennas can be categorized intro directional or omnidirectional
  Based on the radiation pattern of the antenna

## Slide 12: Relationship between antenna size and frequency
Antenna size is inversely proportional to the frequency of radio wave
  Higher the frequency, smaller the antenna size
  Lower frequency, larger is the antenna size
For example:
Dipole: Length of the conductor is half of the wave length of radio wave
Half-wave dipole: Length of conductor is quarter wavelength of radio wave

## Slide 13: Understanding the performance of an antenna
Power output, in a particular direction, compared to that produced in any direction by a perfect omni-directional antenna (isotropic antenna)‏
Effective area: related to physical size and shape of antenna
Relationship between antenna gain and effective area
    G = antenna gain
    Ae = effective area
    f = carrier frequency
    c = speed of light 3 X 108 m/s
    Lambda = carrier wavelength

## Slide 14: Roadmap of the lecture today
Quick Recap
Antenna Continued
Line of Sight and Non Line of Sight
Modulation Basics

## Slide 15: Radiation pattern of the antenna
Radiation pattern of an antenna is a graphical representation of the relative strength of the radiated power in various directions. It illustrates how an antenna distributes energy in space
The radiation pattern is represented as a polar or rectangular plot
Helps you understand the nature of antenna: isotropic, directional or omnidirectional. Helps optimize the placement of wireless devices
Polar Radiation Plot
Rectangular Radiation Plot

## Slide 16: Understanding the antenna beamwidth
Antenna beamwidth is the angular separation between the points on the radiation pattern where the power drops to half of its maximum value, commonly known as the -3 dB points. It defines the directivity and coverage area of the antenna.
Courtesy: EverythingRF

## Slide 17: Understanding the antenna beamwidth
Main lobe of radiation pattern is where maximum radiation occurs
Antenna beamwidth is the angular separation between the points on the radiation pattern where the power drops to half of its maximum value, commonly known as the -3 dB points
Beamwidth defines the directivity and coverage area of the antenna.
Courtesy: EverythingRF

## Slide 18: Beamwidth and antenna gain
What are the implications of the narrow beamwidth?

## Slide 19: Beamwidth and antenna gain
What are the implications of the narrow beamwidth?
  Higher directivity
  Longer range
  Gain?

## Slide 20: Beamwidth and antenna gain
What are the implications of the narrow beamwidth?
  Higher directivity
  Longer range
  Gain? Results in longer range
  Suitable for point-to-point links
What are the implications of the broader beamwidth?

## Slide 21: Beamwidth and antenna gain
What are the implications of the narrow beamwidth?
  Higher directivity
  Longer range
  Gain? Results in longer range
  Suitable for point-to-point links
What are the implications of the broader beamwidth?
  Covers larger area, smaller directivity
  Smaller range
  Gain? Lesser gain
  Suitable for broadcast applications

## Slide 22: Beamwidth and antenna gain
What are the implications of the narrow beamwidth?
  Higher directivity
  Longer range
  Gain? Results in longer range
  Suitable for point-to-point links
What are the implications of the broader beamwidth?
  Covers larger area, smaller directivity
  Smaller range
  Gain? Lesser gain
  Suitable for broadcast applications

## Slide 23: Beamwidth and antenna gain
Parabolic Antenna. Highly Directional.

## Slide 24: Beamwidth and antenna gain
Parabolic Antenna. Highly Directional.
Beamwidth: 0 – 10 degrees

## Slide 25: Beamwidth and antenna gain
Yagi-uda. Directional Antenna.

## Slide 26: Beamwidth and antenna gain
Yagi-uda. Directional Antenna.
Beamwidth: 15 to 40 degrees

## Slide 27: Beamwidth and antenna gain
Dipole Antenna. Somewhat omnidrectional

## Slide 28: Beamwidth and antenna gain
Dipole Antenna. Somewhat omnidrectional
Beamwidth: 70 to 120 degrees

## Slide 29
Wireless Signal Propagation, Modulation, Estimating Range
Notes: ++ Over the past few years, I have designed several backscatter and beyond backscatter systems that precisely overcome these critical challenges that have limited the widespread deployment of backscatter on IoT devices.
++ The research vision that I have pursued and would like to pursue as a faculty member is to enable a massive deployment of IoT devices by bridging the energy asymmetry between sensing, computation and communication blocks by designing novel platforms and communication mechanisms. I am going to describe some of my research contributions next.

## Slide 30: How radio waves propagate to the receiver
Antenna
Transmitting
Device
Radio frequency signal
Receiving Device

## Slide 31: Attenuation and Gain: Decibel (dB) unit
Attenuation: Means loss of energy
  When signal traverses through a medium, it loses energy.
Gain: Means increase in energy
  Often devices such as amplifiers are employed to improve the signal strength
Commonly, we use decibel to calculate gain or loss/attenuation of signal
dB = 10log10P2/P1
  P1 - input signal, P2 - output signal

## Slide 32: Operations in decibel (dB) examples
Suppose a signal travels through a transmission medium and its power decreases to one-half of its original value, meaning that P2 is equal to (1/2)P1. In this scenario, the attenuation, or loss of power, can be determined using the following formula:
Thus, loss of 3 dB, is equivalent to losing half of the signal power

## Slide 33: Operations in decibel (dB) examples
A signal passes through an amplifier, resulting in a tenfold increase in power, expressed as P2 = 10P1. The amplification, also known as the power gain, can be calculated as:
One reason engineers use decibels to measure changes in signal strength is that decibel values can be easily added or subtracted
L1 = 3 dB, L2 = 7 db, Combined loss: 10 dB

## Slide 34: Some common numbers
What does a 10 dB increase in signal represent?

## Slide 35: Some common numbers
What does a 10 dB increase in signal represent?
  10X increase in the signal power
What does a 20 dB increase in signal represent?

## Slide 36: Some common numbers
What does a 10 dB increase in signal represent?
  10X increase in the signal power
What does a 20 dB increase in signal represent?
  100X increase in signal power

## Slide 37: Some common numbers
What does a 10 dB increase in signal represent?
  10X increase in the signal power
What does a 20 dB increase in signal represent?
  100X increase in signal power
What does a 30 dB increase in signal represent?

## Slide 38: Some common numbers
What does a 10 dB increase in signal represent?
  10X increase in the signal power
What does a 20 dB increase in signal represent?
  100X increase in signal power
What does a 30 dB increase in signal represent?
  1000X increase in signal power

## Slide 39: Unit of power of a signal: dBm (decibel milliwatt)
Decibel (dBm) is a measure of signal power, calculated as 10 log10 (Pm) where Pm is power in milliwatts
Example: Calculate the power of a signal with dBm = −30

## Slide 40: Some useful values to remember
3 dB reduction corresponds to a loss of half of the power. 3 dB decrease results in a power that is 50% lower than the original value
0 dBm represents a transmit power of 1 milliwatt (mW). This is commonly used as a reference point in communication systems
30 dBm, which corresponds to a transmit power of 1 watt (W). It is often the maximum permissible output power for devices operating in unlicensed frequency bands, such as those used in Wi-Fi and other wireless communication technologies.

## Slide 41: Roadmap of the lecture today
Quick Recap
Antenna Continued
Line of Sight and Non Line of Sight
Modulation Basics

## Slide 42: How do radio waves propagate from TX to RX?
Medium and environment has an important role to play in propagation
Radio waves do not propagate well underwater. Submarines uses sound
Environment impacts the radio wave propagation significantly
  Reduced communication range
  Interference from other devices
  Issues with reliability
  …… and many more

## Slide 43: Radio waves propagation in line-of-sight
Transmitting and receiving antennas must be within line of sight
Satellite communication – signal above 30 MHz not reflected by ionosphere
Ground communication – antennas in effective line of site due to refraction

## Slide 44: Long range wireless transmissions using IoT devices

## Slide 45: Estimating received signal strength and range: Friis propagation model
  fc is the center frequency in Hz
  c is speed of light
  d is the distance between transmitter and receiver
  Alpha is the path loss component
  G is antenna gain

## Slide 46: Path Loss Exponent
2 to 3
Obstructed in factory
Rapport, Table 4.2, pp139
4 to 6
Obstructed in building
1.6 to 1.8
In building LOS
3 to 5
Shadowed urban cellular radio
2.7 to 3.5
Urban area cellualr radio
2
Free Space
Path Loss Exponential ()
Environment

## Slide 47: Radio propagation is complex in real-world, especially when obstacles are present

## Slide 48: Non-line of sight propagation of radio waves
Transmitter and receiver are not kept in line of sight
Radio waves encounter obstacles, may go through walls, buildings
Much more applicable to read world environment and deployments
Significantly impacts the communication range and reliability

## Slide 49: Example: Range and antenna gain estimation
Question: A wireless receiver with an effective radius of 100cm is receiving signals at 2 GHz from a transmitter that transmits at a power of 100W and a gain of 40dB (or 10,000). Assume path loss exponent is 2.
What is the gain of the receiver antenna?
What is the received power if the receiver is 1km away from the transmitter?
If the receiver is receiving signals at 900 MHz frequency (instead of 2GHz), please calculate (a) and (b) again?
What do you notice and why?

## Slide 50: Total link gain in wireless communication
Total link gain represents the net amplification and attenuation of the electromagnetic signal along the communication path
What are the factors that are included in the total link gain?

## Slide 51: Total link gain in wireless communication
Total link gain represents the net amplification and attenuation of the electromagnetic signal along the communication path
What are the factors that are included in the total link gain?
  Antennas
  Free space path loss
  And other system component
Gtx = Transmitter antenna gain (dB)
Grx= Receiver antenna gain (dB)
LPath = Path loss (dB), including free-space loss
LMisc= Miscellaneous losses (dB), such as atmospheric losses, cable losses, and interference effects

## Slide 52: Let us look at another example
Question: Two office buildings 1 km apart are connected via a point-to-point microwave link operating at 5 GHz. High-gain directional antennas of similar type are used on both sides to ensure minimal signal loss.
If each of the antenna has an effective area of 0.05 m2
What is the total link gain?

## Slide 53: Link Budget and Total Link Gain
Calculation that takes into account all gains and losses to determine received signal strength of wireless signal in a communication system
Total Link Budget (Prx) = Ptx + Total Link Gain

## Slide 54: Previous year’s assessment question
Question: Over the past several years, we have seen a growing interest in utilizing satellites to provide wireless connectivity to Internet of Things (IoT) devices. These satellites usually operate at altitudes of 400 to 500 kilometers from the Earth's surface. However, this deployment of satellites has led to concerns regarding orbital congestion and pollution. As an alternative, high-altitude balloons are being explored to provide network connectivity to Internet of things devices. These balloons fly at much lower altitudes of around 20 kilometers from earth’s surface and they offer a very cost-effective solution to satellite launches.

## Slide 55: Google Project Loon? Do you know?
Google Project Loon: https://x.company/projects/loon/

## Slide 56: One of the last year’s question
If you are using low-altitude balloons to provide connectivity to ground based IoT devices. Please answer the following questions:
What type of antennas are suitable for use on the high-altitude balloons and ground based IoT devices to ensure reliable communication?
Provide appropriate rationale for your choice

## Slide 57: One of the last year’s question
If you are using low-altitude balloons to provide connectivity to ground based IoT devices. Please answer the following questions:
What type of antennas are suitable for use on the high-altitude balloons and ground based IoT devices to ensure reliable communication?
Provide appropriate rationale for your choice
ANSWER:
Balloon - We can use directional antenna such as parabolic antenna to ensure the energy is directed towards the deployment of IoT device.
On IoT devices - Omnidirectional antennas, as it can allow them to receive energy from any direction even if these devices are mobile. It would allow us to avoid positioning the nodes with limited line-of-sight to the balloon.

## Slide 58: One of the last year’s question
(b) Which frequency bands are suitable for communication between balloon and IoT device? Provide appropriate rationale for your choice. (1 point)

## Slide 59: One of the last year’s question
(b) Which frequency bands are suitable for communication between balloon and IoT device? Provide appropriate rationale for your choice. (1 point)
ANSWER:
Sub-GHz bands due to their superior propagation characteristics. Ideally, we should be looking at ISM frequency bands.
For some application, perhaps, 2.4 GHz may work.

## Slide 60: One of the last year’s question
(c) From a wireless communication perspective, what are two advantages and disadvantages of using balloons for connectivity in IoT devices compared to satellite-based solutions? (2 point)

## Slide 61: One of the last year’s question
(c) From a wireless communication perspective, what are two advantages and disadvantages of using balloons for connectivity in IoT devices compared to satellite-based solutions? (2 point)
ANSWER:
There can be several advantages:
1. Lower latency owing to lower altitude of the balloon
2. We can use ISM frequency bands due to shorter distances for communication
3. Better signal quality owing to stronger signals
Cons:
1. Limited coverage when compared to satellites, may require several balloons overhead
2. Greater chance of interference with terrestrial and other such transmissions
3. Higher maintenance overhead to replace and maintain balloons

## Slide 62: One of the last year’s question
(d) Given that the IoT device is equipped with a radio with a receive sensitivity of -100 dBm and an antenna gain of 2 dB. There is an estimated distance of 20 kilometers between the balloon and the IoT device, and the balloon is equipped with 8 dB antenna. Please calculate the transmit power required at the balloon to ensure successful packet reception at IoT device. Use the frequency selected in part (b) for your calculations. The path loss exponent is 2. (4 point)

## Slide 63: Roadmap of the lecture today
Quick Recap
Antenna Continued
Line of Sight and Non Line of Sight
Modulation Basics

## Slide 64: How are radio waves modified to carry information
Encoding information “baseband" in an analog “carrier” signal
  Baseband signal often much lower in frequency than the carrier
  Frequency of the carrier signal dictates the part of the radio spectrum
Why? baseband signals or information change is at much lower rate
  Speech: upto 20 KHz, temperature changes – few Hz
  Enables a better usage of the radio spectrum
  Enables communication among several devices sharing the spectrum
Modulation
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 65: What are different modulation techniques?
Vary frequency, amplitude, phase of carrier signal according message signal
  We can also vary them together to support complex modulation schemes
  Analog and Digital counterparts of these modulation schemes exist
Modulation
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 66: Amplitude modulation: vary amplitude of carrier signal
Change amplitude of a carrier signal according to the message signal
Simplest and the earliest modulation technique
Remains widely used for radio broadcast, also computer communication
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 67: Amplitude modulation: vary amplitude of carrier signal
Ac = Carrier amplitude
Am = Modulating (baseband) signal amplitude
m(t) = Message signal
fc = Carrier frequency

## Slide 68: Modulation Index
Signifies the extent to which the carrier signal is modulated with the message signal. It determines the strength of the modulated signal, impacts bandwidth, and also power distribution and overall signal quality
For amplitude modulation = Am/Ac
  Am= Peak amplitude of modulating/baseband signal
  Ac = Peak amplitude of carrier signal

## Slide 69: Significance of modulation index ()
< 1
  Carrier is not fully modulated
  No distortion but the signal maybe weak
1
  Carrier is fully modulated
1
  Overmodulation, signal is distorted leads to clipping

## Slide 70: Amplitude modulation example
You are given a carrier signal with the frequency of 100 KHz and amplitude of 5. It is modulated using amplitude modulation (double side band, full carrier) with a message/baseband signal of the frequency 5 KHz and amplitude 2.
Please determine modulation index and mathematical expression representing the modulated signal?

## Slide 71: Frequency modulation: vary frequency of carrier signal
Change frequency of a carrier signal according to the message signal
Advantages (over AM): Resilient to interference, spectrum efficiency
Remains widely used for radio broadcast, also computer communication
First demonstrated by Armstrong in 1935!
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 72: Frequency modulation: vary frequency of carrier signal
Ac = Carrier amplitude
fc = Carrier frequency
kf = Frequency sensitivity of the modulator (how much the carrier frequency changes in response to the amplitude of the modulating signal)
m(t) = Modulating signal
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 73: Modulation Index of frequency modulated signal
Where,
f = Peak frequency deviation (how much the carrier frequency changes)
fm = Maximum frequency of the modulating signal
< 1 : Narrow band signal
> 1 : Wideband signal, better noise immunity, signal quality, FM broadcasts
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 74: Bandwidth of frequency modulated signals
Given by the Carson’s rule
Bandwidth of a frequency modulated signal is 2 (+ )
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 75: Phase modulation: vary phase of carrier signal
Change phase of a carrier signal according to the message signal
It is an integral part of modern communication standards: WiFi, Television
Advantages (over FM): Better SNR, spectral efficiency
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 76: Digital equivalent of the AM, FM and PM modulation
Digital variant of these schemes vary analog signal according to digital bits
  ASK: amplitude shift keying
  FSK: frequency shift keying
  PSK: phase shift keying
Digital variants relevant when we talk about computer communication
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 77: Even more complex modulation schemes exist
Builds on simple modulation schemes AM, FM, PM (or digital equivalent)
Briefly cover some during later part of the course
Complex modulation schemes ensure better performance
  Spectral efficiency
  Higher range
  Higher throughput
  ……
Choice of the modulation scheme depends on the target application
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 78: Roadmap of the lecture today
Quick Recap
Antenna Continued
Line of Sight and Non Line of Sight
Modulation Basics

## Slide 79: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.