## Slide 1: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.

## Slide 2: Roadmap of the lecture today
Quick Recap
Antenna Continued
Line of Sight and Non Line of Sight
Modulation Basics

## Slide 3
Quick Recap
Notes: ++ Over the past few years, I have designed several backscatter and beyond backscatter systems that precisely overcome these critical challenges that have limited the widespread deployment of backscatter on IoT devices.
++ The research vision that I have pursued and would like to pursue as a faculty member is to enable a massive deployment of IoT devices by bridging the energy asymmetry between sensing, computation and communication blocks by designing novel platforms and communication mechanisms. I am going to describe some of my research contributions next.

## Slide 4: Radiation pattern of the antenna
Radiation pattern of an antenna is a graphical representation of the relative strength of the radiated power in various directions. It illustrates how an antenna distributes energy in space
The radiation pattern is represented as a polar or rectangular plot
Helps you understand the nature of antenna: isotropic, directional or omnidirectional. Helps optimize the placement of wireless devices
Polar Radiation Plot
Rectangular Radiation Plot

## Slide 5: Understanding the antenna beamwidth
Main lobe of radiation pattern is where maximum radiation occurs
Antenna beamwidth is the angular separation between the points on the radiation pattern where the power drops to half of its maximum value, commonly known as the -3 dB points
Beamwidth defines the directivity and coverage area of the antenna.
Courtesy: EverythingRF

## Slide 6: Beamwidth and antenna gain
What are the implications of the narrow beamwidth?
  Higher directivity
  Longer range
  Gain? Results in longer range
  Suitable for point-to-point links
What are the implications of the broader beamwidth?
  Covers larger area, smaller directivity
  Smaller range
  Gain? Lesser gain
  Suitable for broadcast applications

## Slide 7: Non-line of sight propagation of radio waves
Transmitter and receiver are not kept in line of sight
Radio waves encounter obstacles, may go through walls, buildings
Much more applicable to read world environment and deployments
Significantly impacts the communication range and reliability

## Slide 8
Revisiting antennas and their gain
Yagi-uda antenna. It has a very high gain. The gain and directionality increases with the number of antenna elements.
Antenna Gain: 23 dBi
Antenna Gain: 8 dBi

## Slide 9
Revisiting antennas and their gain
Chip antenna makes sacrifice due to smaller form factor and hence the least gain. Whip antenna has less directionality than Yagi-uda antenna.
Antenna Gain: -1 dBi
Antenna Gain: 3.8 dBi

## Slide 10: Basics of wireless communication and networking
Free space path loss (FSPL or FSL): The loss of power encountered by signal as it transmits from the transmitter to the receiver
d is the distance between the transmitter and receiver antennas (in meters),
f is the frequency of the signal (in Hertz),
c is the speed of light in a vacuum

## Slide 11: Total link gain in wireless communication
Total link gain represents the net amplification and attenuation of the electromagnetic signal along the communication path
What are the factors that are included in the total link gain?
  Antennas
  Free space path loss
  And other system component
Gtx = Transmitter antenna gain (dB)
Grx= Receiver antenna gain (dB)
LPath = Path loss (dB), including free-space loss
LMisc= Miscellaneous losses (dB), such as atmospheric losses, cable losses, and interference effects

## Slide 12: Link Budget and Total Link Gain
Calculation that takes into account all gains and losses to determine received signal strength of wireless signal in a communication system
Total Link Budget (Prx) = Ptx + Total Link Gain

## Slide 13: Revisiting dB, dBm, and dBi, and operations
Let us recall the definition of all three of them:
dB (Decibel):
  Logarithmic unit for ratios (gain/loss).
  Dimensionless (e.g., 3 dB amplifier gain).
dBm:
  Absolute power referenced to 1 mW.
  0 dBm = 1 mW (e.g., 20 dBm = 100 mW).
dBi:
  Antenna gain relative to an isotropic radiator.
  Measures directionality (e.g., 5 dBi = 5 dB over isotropic).

## Slide 14: Adding and Subtracting dB, dBm, and dBi
✅ Adding dB values:
• If two components contribute gain or loss, we add their dB values
• Example: Two amplifiers with +10 dB and +5 dB gain
✅ Adding dBi to dBm to get EIRP:
• Effective Isotropic Radiated Power (EIRP) is the total output power including antenna gain
• Example:
• Transmit Power = 20 dBm
• Antenna Gain = 8 dBi
EIRP = 20 + 8 = 28 dBm

## Slide 15: Adding and Subtracting dB, dBm, and dBi
✅ Subtracting Losses (dB) from Power (dBm)
Losses (such as cable loss, free-space path loss) can be subtracted from the transmitted power.:
Transmit Power = 30 dBm, Antenna Gain = 5 dBi, Cable Loss = 2 dB, Path Loss = 50 dB
Receiver Antenna Gain = 3 dBi
Prx= 30 + 5 - 2 - 50 + 3 = -14 dBm
✅ Subtracting dBm values to get dB difference
If you want to compare two power levels, you can subtract them in dB:
Delta P = P1 - P2
Power at point A = 20 dBm, Power at point B = 5 dBm
Difference in power: 20 - 5 = 15 dB
This means B has 15 dB less power than A.

## Slide 16: Adding and Subtracting dB, dBm, and dBi
❌ You cannot add dBm values directly
• Example (incorrect):
10 dBm + 20 dBm = 30 dBm
Why? Because dBm represents absolute power, and logarithmic values cannot be added directly.
Instead, convert to linear scale:
10 dBm = 10 mW
20 dBm = 100 mW
Total Power = 110 mW
Convert back to dBm: Ptotal = 10log10(110) = 20.4 dBm

## Slide 17: Adding and Subtracting dB, dBm, and dBi
Do:
Use dB ± dBm for power adjustments (e.g., Tx power + antenna gain).
Subtract dBm - dBm to compute ratios (e.g., SNR calculations).
Add dBi only to dBm for EIRP.
Don’t:
Add dBm + dBm or dBi + dBi.
Mix units without context (e.g., dBi + dBm ≠ dB).
Why:
dB = ratio; dBm = absolute power; dBi = directional gain.
Antenna gains are standalone; powers require linear conversion.

## Slide 18: Adding and Subtracting dB, dBm, and dBi
dBm + dBm:
Invalid! Powers require linear addition (e.g., 20 dBm + 20 dBm ≠ 40 dBm).
dBi + dBi:
Antenna gains are not additive (e.g., 3 dBi + 3 dBi ≠ 6 dBi).
Mismatched Contexts:
E.g., Adding Rx antenna gain (dBi) directly to Tx power (dBm) without path loss

## Slide 19: Wireless link quality and reliability
Link reliability metrics quantify the quality and stability of wireless links
Wireless links are inherently unstable due to interference, multipath fading, and mobility. Reliable communication requires choosing links that offer consistent performance. These metrics aid in designing robust protocols for routing, load balancing, and link adaptation.
  Helps in routing decisions, optimizing network performance, and improving communication reliability among other uses
  From application perspective, no buffering, less latency etc

## Slide 20: Wireless link quality and reliability
Important link quality metrics that we consider in wireless networking:
  Packet Delivery Ratio (PDR): Ratio of received packets to transmitted packets
  Bit Error Rate (BER): Measures the number of bit errors per unit time
  Signal-to-Noise Ratio (SNR): Higher SNR indicates better link quality
  Expected Transmission Count (ETX): Predicts the number of transmissions required for successful delivery

## Slide 21: Packet Delivery Ratio (PDR)
Ratio of successfully received packets to transmitted packets.
Measures network reliability
PDR = X 100
Significance: Higher PDR indicates better link quality, Low PDR suggests congestion, interference, or poor connectivity

## Slide 22: Examples
Question: A sensor node transmits 1000 packets, and the receiver successfully gets 900? What is the PDR?

## Slide 23: Examples
Question: A sensor node transmits 1000 packets, and the receiver successfully gets 900? What is the PDR?
Answer:
PDR = X 100 = 90%

## Slide 24: Bit Error Rate (BER)
Ratio of bits received in error to the total transmitted bits
Indicates transmission quality at the physical layer.
BER = X 100
Significance: A lower BER means fewer errors and better link performance, Higher BER leads to data corruption and retransmissions

## Slide 25: Perspective on Bit Error Rate (BER)
Some perspective on bit error rate values for wired and wireless:
Wired Ethernet: 10⁻¹² (very low errors)
• Wireless Wi-Fi: 10⁻⁶ to 10⁻³ (moderate errors)
• Poor wireless conditions: 10⁻² (high errors)

## Slide 26: Examples
Question: A 128-byte packet (1024 bits) is sent with a BER of 10⁻³. How many errors are there per-packet?

## Slide 27: Examples
Question: A 128-byte packet (1024 bits) is sent with a BER of 10⁻³. How many errors are there per-packet?
Answer: 1024 X 10-3 = 1.024 = 1 bit error / packet

## Slide 28: Signal-to-Noise Ratio (SNR)
Ratio of signal power to background noise, often measured in decibels (dB)
SNR = 10log10( )
Significance:
  Higher SNR → Stronger signal, fewer errors
  Lower SNR → Weaker signal, more packet loss
  SNR < 10 dB can lead to frequent disconnections.

## Slide 29: Perspective on Signal to Noise Ratio
Some perspective on SNR values:
>25 dB: Excellent (High-speed Wi-Fi, 4G LTE)
• 15-25 dB: Good (Usable but may have errors)
• <10 dB: Poor (Likely unreliable)

## Slide 30: Examples
Question: A Wi-Fi user has a signal power of -50 dBm and noise power of -80 dBm. What is the SNR?
Answer:
SNR = (-50) - (-80) = 30 dB

## Slide 31: Expected Transmission Count (ETX)
Measures the expected number of transmissions (including retransmissions) required for a packet to be successfully receive
Used in routing algorithms (e.g., wireless mesh networks)
ETX =
Significance:
  Lower ETX means fewer retransmissions and better efficiency.
  High ETX leads to increased latency and power consumption

## Slide 32: Understanding Channel Capacity & Link Quality
Definition: Maximum rate at which information can be transmitted over a communication channel without error
Channel capacity is measured in the unit of bits/second
How does channel capacity relate to the link quality?

## Slide 33: Understanding Channel Capacity & Link Quality
Definition: Maximum rate at which information can be transmitted over a communication channel without error
Channel capacity is measured in the unit of bits/second
How does channel capacity relate to the link quality?
  Higher SNR usually leads to a higher capacity
  Recall bandwidth is the frequency range over which the signal is transmitted; a wider bandwidth can support higher data rates
  Factors that reduce link quality?

## Slide 34: Understanding Channel Capacity & Link Quality
Definition: Maximum rate at which information can be transmitted over a communication channel without error
Channel capacity is measured in the unit of bits/second
How does channel capacity relate to the link quality?
  Higher SNR usually leads to a higher capacity
  Recall bandwidth is the frequency range over which the signal is transmitted; a wider bandwidth can support higher data rates
  Factors that reduce link quality? Fading, interference, reduce channel capacity

## Slide 35: Understanding Channel Capacity & Link Quality
Definition: Maximum rate at which information can be transmitted over a communication channel without error
Channel capacity is measured in the unit of bits/second
How does channel capacity relate to the link quality?
  Higher SNR usually leads to a higher capacity
  Recall bandwidth is the frequency range over which the signal is transmitted; a wider bandwidth can support higher data rates
  Factors that reduce link quality? Fading, interference, reduce channel capacity
Takeaways:
Good link quality (high SNR, low interference) improves channel capacity
Poor link quality leads to lower achievable data rates, even if the theoretical channel capacity is high

## Slide 36: Channel Capacity & Link Quality – The Shannon Perspective
Shannon’s Channel Capacity Formula:
C = B X log2(1+)
C : Channel capacity in bits per second (bps)
• B : Bandwidth of the channel in Hertz (Hz)
• S/N : Signal-to-noise ratio (SNR), expressed as a linear ratio

## Slide 37: Example
Available Bandwidth (B): 20 MHz
Signal-to-Noise Ratio (S/N): 30 dB
What is the channel capacity?

## Slide 38: Example
Total Available Bandwidth: 20 MHz
Channel Structure: Divided into 4 equal subchannels (5 MHz wide)
SNR Values (in dB) for Each Subchannel:
  Subchannel 1: 20 dB
  Subchannel 2: 25 dB
  Subchannel 3: 30 dB
  Subchannel 4: 35 dB
What is the overall channel capacity?

## Slide 39: Takeaway from the example and discussion
Different parts of the channel experience varying SNR levels. Calculating capacity per subchannel allows us to capture these variations.
The overall channel capacity is the sum of the capacities of the individual subchannels
In practice, factors such as channel fading, interference, and implementation losses might reduce the achievable capacity below this theoretical maximum
Wireless networks strive to maximize SNR and minimize interference to approach the theoretical capacity
Link quality assessments help determine if network conditions are suitable for high-data-rate applications

## Slide 40: Roadmap of the lecture today
Quick Recap
Antenna Continued
Line of Sight and Non Line of Sight
Modulation Basics

## Slide 41: How are radio waves modified to carry information
Encoding information “baseband" in an analog “carrier” signal
  Baseband signal often much lower in frequency than the carrier
  Frequency of the carrier signal dictates the part of the radio spectrum
Why? baseband signals or information change is at much lower rate
  Speech: upto 20 KHz, temperature changes – few Hz
  Enables a better usage of the radio spectrum
  Enables communication among several devices sharing the spectrum
Modulation
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 42: What are different modulation techniques?
Vary frequency, amplitude, phase of carrier signal according message signal
  We can also vary them together to support complex modulation schemes
  Analog and Digital counterparts of these modulation schemes exist
Modulation
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 43: Amplitude modulation: vary amplitude of carrier signal
Change amplitude of a carrier signal according to the message signal
Simplest and the earliest modulation technique
Remains widely used for radio broadcast, also computer communication
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 44: Amplitude modulation: vary amplitude of carrier signal
Ac = Carrier amplitude
Am = Modulating (baseband) signal amplitude
m(t) = Message signal
fc = Carrier frequency

## Slide 45: Modulation Index
Signifies the extent to which the carrier signal is modulated with the message signal. It determines the strength of the modulated signal, impacts bandwidth, and also power distribution and overall signal quality
For amplitude modulation = Am/Ac
  Am= Peak amplitude of modulating/baseband signal
  Ac = Peak amplitude of carrier signal

## Slide 46: Significance of modulation index ()
< 1
  Carrier is not fully modulated
  No distortion but the signal maybe weak
1
  Carrier is fully modulated
1
  Overmodulation, signal is distorted leads to clipping

## Slide 47: Amplitude modulation example
You are given a carrier signal with the frequency of 100 KHz and amplitude of 5. It is modulated using amplitude modulation (double side band, full carrier) with a message/baseband signal of the frequency 5 KHz and amplitude 2.
Please determine modulation index and mathematical expression representing the modulated signal?

## Slide 48: Frequency modulation: vary frequency of carrier signal
Change frequency of a carrier signal according to the message signal
Advantages (over AM): Resilient to interference, spectrum efficiency
Remains widely used for radio broadcast, also computer communication
First demonstrated by Armstrong in 1935!
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 49: Frequency modulation: vary frequency of carrier signal
Ac = Carrier amplitude
fc = Carrier frequency
kf = Frequency sensitivity of the modulator (how much the carrier frequency changes in response to the amplitude of the modulating signal)
m(t) = Modulating signal
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 50: Modulation Index of frequency modulated signal
Where,
f = Peak frequency deviation (how much the carrier frequency changes)
fm = Maximum frequency of the modulating signal
< 1 : Narrow band signal
> 1 : Wideband signal, better noise immunity, signal quality, FM broadcasts
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 51: Bandwidth of frequency modulated signals
Given by the Carson’s rule
Bandwidth of a frequency modulated signal is 2 (+ )
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 52: Frequency modulation example
An FM transmitter broadcasts audio signals with a maximum modulating frequency (fm) of 3 kHz and is designed with a peak frequency deviation ( f) of 15 kHz.
Define the modulation index in the context of FM and calculate its value for this transmitter
Using Carson’s Rule, calculate the approximate total bandwidth required for this FM signal

## Slide 53: Frequency deviation, Carson’s Rule, Takeaway
Frequency deviation (f) is the maximum departure of the instantaneous frequency of the FM signal from the carrier frequency due to modulation
Determines the extent of frequency variation, which in turn affects the transmitted signal’s spectrum
Carson’s rule provides a practical estimate of the bandwidth by accounting for the significant sidebands that contain most of the signal’s power. Ensures that the majority of the signal’s power is transmitted within the calculated bandwidth, making it a valuable tool for system planning and regulatory compliance.

## Slide 54: Phase modulation: vary phase of carrier signal
Change phase of a carrier signal according to the message signal
It is an integral part of modern communication standards: WiFi, Television
Advantages (over FM): Better SNR, spectral efficiency
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 55: Digital equivalent of the AM, FM and PM modulation
Digital variant of these schemes vary analog signal according to digital bits
  ASK: amplitude shift keying
  FSK: frequency shift keying
  PSK: phase shift keying
Digital variants relevant when we talk about computer communication
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 56: Even more complex modulation schemes exist
Builds on simple modulation schemes AM, FM, PM (or digital equivalent)
Briefly cover some during later part of the course
Complex modulation schemes ensure better performance
  Spectral efficiency
  Higher range
  Higher throughput
  ……
Choice of the modulation scheme depends on the target application
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 57: What are components of internet of things
Computation and Storage
Sensing and Actuation
Power
Wireless Connectivity
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 58: Microcontrollers are heart of embedded systems
A microcontroller (µC) is a small computer on a single integrated circuit consisting of a relatively simple central processing unit (CPU) combined with peripheral devices such as memories, I/O devices, and timers
More than half of all CPUs sold are microcontroller (and growing)
Low-power, often includes sleep mode that dramatically reduces the power consumed to micro or even nanowatts
Notes: Backscatter communication actually help us overcome this limitation

## Slide 59: What is heart of computers and internet of things
Microprocessor (Computers)
  They usually don’t have peripherals or memory
  CPU + Pins (No memory, peripherals)
  Your computer typically has a microprocessor
Microcontrollers (Internet of Things)
  Memory + Peripherals + CPU + Pins
  Peripherals: Specialized hardware units within the chip
Notes: Backscatter communication actually help us overcome this limitation

## Slide 60: What is a microcontroller? Microprocessor + Peripherals + Memory + Pins + ?
Microcontroller
Processor
Memory
Peripherals
Pins
Notes: Backscatter communication actually help us overcome this limitation

## Slide 61: System on chips
System on chips (SoC)
  Microcontroller + Extensive Peripherals
  Essentially multiple chips combined
  Example: Radios, ML accelerators in a single chip
Notes: Backscatter communication actually help us overcome this limitation

## Slide 62: An image of the die of a microcontroller

## Slide 63: Instruction set architecture and realization
Instruction set architecture (ISA): It is the definition of the instructions that the processor can execute and certain structural constraints (such as word size) that realizations must share.
Processor, Realization, Chip: Piece of silicon sold by a vendor which is the realization of the ISA.
A ISA may appear in many different chips, often made by different manufacturers, and often having widely varying performance profiles.
Advantages?

## Slide 64: Instruction set architecture and realization
Instruction set architecture (ISA): It is the definition of the instructions that the processor can execute and certain structural constraints (such as word size) that realizations must share.
Processor, Realization, Chip: Piece of silicon sold by a vendor which is the realization of the ISA.
A ISA may appear in many different chips, often made by different manufacturers, and often having widely varying performance profiles.
Advantages? Sharing an ISA in a family of processors is that software tools, which are costly to develop, may be shared, and (sometimes) the same programs may run correctly on multiple realizations.

## Slide 65: Instruction set architecture and realization
Instruction set architecture (ISA): It is the definition of the instructions that the processor can execute and certain structural constraints (such as word size) that realizations must share.
Processor, Realization, Chip: Piece of silicon sold by a vendor which is the realization of the ISA.
Does ARM make it’s own chip? What is Cortex-M series?
What are some ISAs? And chip you can recall?

## Slide 66: Other embedded microcontroller architectures
Motorola 6800
Intel 8080
Intel 8051
Atmel AVR
ARM
Motorola Coldfire
MIPS
PowerPC
............

## Slide 67: Some example of older microcontrollers
Cheap , small computer systems
PIC
  8, 16, and 24-bit MIPs architecture
  PICAXE available with Basic interpreter
AVR
  8-bit custom architecture (AVR architecture)
  Used in Arduinos
  AT Tiny 4: $0.30 per unit
    4 I/O pins, 32 Bytes RAM, 512 Bytes ROM

## Slide 68: More capable microcontrollers (00s-10s)
Diversify into extreme low power and more capable systems
MSP430
  16-bit custom architecture (MSP430 architecture)
  Capable, but also extremely low power
    <1 μA sleep current
STM32, Atmel SAM series (Cortex-M0, M3, M4, M4F)
  32-bit ARM architecture (ARMv7)
    Leverage success of ARM on smartphones
  Every peripheral under the sun. Plus a variety of memory choices

## Slide 69: ARM Cortex M Series
A number of options for increasing capabilities
In practice:
  Cortex-M0+ for low-end systems
  Coretx-M4 for high capability systems

## Slide 70: Digital Signal Processor
Many embedded applications require performing of signal processing. Can you think of some embedded applications?
Characteristics of application requiring signal processing:
  Deal with large amounts of information
  Sample in time, space or both
  Sophisticated mathematical operations like filtering, frequency analysis
Digital signal processor are class of processors optimized for such mathematically intensive tasks

## Slide 71: Digital Signal Processor
Many embedded applications require performing of signal processing. Can you think of some embedded applications?
Characteristics of application requiring signal processing:
  Deal with large amounts of information
  Sample in time, space or both
  Sophisticated mathematical operations like filtering, frequency analysis
Digital signal processor are class of processors optimized for such mathematically intensive tasks

## Slide 72: Multicore and Multiprocessor architecture
A multicore consists of more than one processor on a single chip
Existed since 1990’s, but has seen a great uptake recently
Becoming more and more relevant for embedded systems
Heterogeneous multicore: Combines different processors on a single chip. Even following different ISAs.
Applications which require multicore architecture?

## Slide 73: What are trends for future microcontrollers
Multi-core systems
  Not for performance, but for separation of concerns
    Run radio code on one core
    Application code goes on the other core
  Also allows BIG.little architecture
    Higher performance core when interpreting data
    Lower performance core for sampling sensors
  nRF53 series is already doing this
    But support is still nascent

## Slide 74: Raspberry Pi Pico: Multiple cores, Low-power

## Slide 75: Microcontrollers with neural networks
Very low-power for specific tasks. Voice detection at hundreds of microwatts of power consumption

## Slide 76: Memory on microcontroller (hierarchy)
Registers
RAM
ROM

## Slide 77: Example of volatile memory: SRAM
Same design as registers in traditional computer systems
  No need to refresh it -> lower energy costs
Tradeoff:
  More expensive
  Physically larger

## Slide 78: Example of non-volatile memory: Flash
Same design as SSDs and Flash drives
Memory is stored with no energy costs
  Reading is lowish energy and quick
  Writing is high energy and very slow
    Writing also has to occur in blocks (e.g. 512 bytes)
Concern: Flash has a limited lifetime ~10,000 writes
  Only writing to Flash when you load code? Essentially forever
  Recording data to Flash every second? 2.8 hours

## Slide 79: SRAM (RAM) versus Flash (ROM)
Size and time difference between non-volatile and volatile memory is significantly reduced from traditional computing
  Non-volatile store 2-10x larger than volatile
  Single-cycle RAM. Maybe two-cycles to Flash (to read)
Major difference: energy and writability
  SRAM is low-energy to read and write (no refresh needed)
  Flash is lowish-energy to read, but very high energy to write
Hierarchical structure is not enforced
  Same address space for RAM and Flash (very different from traditional)
  Run instructions right inside of Flash
  Keep variables in RAM (or const variables in Flash)

## Slide 80: Emerging non-volatile memories FRAM , MRAM
FRAM and MRAM are both rising protentional Flash replacements
  Non-volatile
  Writable at the byte level
  Very high to infinite write/erase cycles
  Lower energy costs for writing and reading
The two-use unrelated magnetic techniques for data storage
Starting to appear in microcontrollers
  TI MSP430s have used 16 kB FRAM
  Apollo4 (ARM Cortex-M4F) has 2 MB of MRAM

## Slide 81: History of the Contiki operating system
Started in Sweden! Started by – Adam Dunkels
Awarded 2022 SenSys Test-of-Time Award for Protothreads (2004)
Companies and universities developing (or has contributed) Contiki OS:
  SAP, Cisco, Atmel, NewAE and others
  SICS, TU Munich and others

## Slide 82: Contiki operating system: Hello, World!
}
PROCESS_END();
#include “contiki.h”
#include <stdio.h>
PROCESS(hello_world_process, “hello world”); AUTOSTART_PROCESSES(&hello_world_process); PROCESS_THREAD(hello_world_process, ev, data)
{
PROCESS_BEGIN();
// initialize statements come here
printf(“Hello world!\n\r”);
while(1) {
// perform tasks here
// PROCESS_WAIT_EVENT();

## Slide 83: Hardware Platform: CC2650 SensorTag
Processor: ARM Cortex M3 32-bit processor, up to 48-MHz clock speed
Memory: 8KB of SRAM for Cache, 20KB of SRAM, 128KB of In-System Programmable Flash
Network: 6LoWPAN, Bluetooth Low energy, RF4CE, ZigBee
10 sensors including support for light, digital microphone, magnetic sensor, humidity, pressure, accelerometer, gyroscope, magnetometer, object temperature, and ambient temperature

## Slide 87: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.